## Slide 1: Computer Organization & Assembly Language - EE2003

## Slide 2: Lecture 15
Week 09

## Slide 3: Chapter Overview
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Conditional Control Flow Directives

## Slide 4: Boolean and Comparison Instructions
CPU Status Flags
AND Instruction
OR Instruction
XOR Instruction
NOT Instruction
Applications
TEST Instruction
CMP Instruction

## Slide 5: Status Flags - Review
The Zero flag is set when the result of an operation equals zero.
The Carry flag is set when an instruction generates a result that is too large (or too small) for the destination operand.
The Sign flag is set if the destination operand is negative, and it is clear if the destination operand is positive.
The Overflow flag is set when an instruction generates an invalid signed result (bit 7 carry is XORed with bit 6 Carry).
The Parity flag is set when an instruction generates an even number of 1 bits in the low byte of the destination operand.
The Auxiliary Carry flag is set when an operation produces a carry out from bit 3 to bit 4

## Slide 6: AND Instruction
Performs a Boolean AND operation between each pair of matching bits in two operands
Syntax:
    AND destination, source
  (same operand types as MOV)
AND

## Slide 7: OR Instruction
Performs a Boolean OR operation between each pair of matching bits in two operands
Syntax:
    OR destination, source
OR

## Slide 8: XOR Instruction
Performs a Boolean exclusive-OR operation between each pair of matching bits in two operands
Syntax:
    XOR destination, source
XOR
XOR is a useful way to toggle (invert) the bits in an operand.

## Slide 9: NOT Instruction
Performs a Boolean NOT operation on a single destination operand
Syntax:
    NOT destination
NOT

## Slide 10: Bit-Mapped Sets
Binary bits indicate set membership
Efficient use of storage
Also known as bit vectors

## Slide 11: Bit-Mapped Set Operations
Set Complement
    mov eax,SetX
    not eax
Set Intersection
    mov eax,setX
    and eax,setY
Set Union
    mov eax,setX
    or eax,setY

## Slide 12: Applications (1 of 5)
mov al,'a' ; AL = 01100001b
and al,11011111b ; AL = 01000001b
Task: Convert the character in AL to upper case.
Solution: Use the AND instruction to clear bit 5.

## Slide 13: Applications (2 of 5)
mov al,6 ; AL = 00000110b
or al,00110000b ; AL = 00110110b
Task: Convert a binary decimal byte into its equivalent ASCII decimal digit.
Solution: Use the OR instruction to set bits 4 and 5.
The ASCII digit '6' = 00110110b

## Slide 14: Applications (3 of 5)
mov ax,40h ; BIOS segment
mov ds,ax
mov bx,17h ; keyboard flag byte
or BYTE PTR [bx],01000000b ; CapsLock on
Task: Turn on the keyboard CapsLock key
Solution: Use the OR instruction to set bit 6 in the keyboard flag byte at 0040:0017h in the BIOS data area.
This code only runs in Real-address mode, and it does not work under Windows NT, 2000, or XP.

## Slide 15: Applications (4 of 5)
mov ax,wordVal
and ax,1 ; low bit set?
jz EvenValue ; jump if Zero flag set
Task: Jump to a label if an integer is even.
Solution: AND the lowest bit with a 1. If the result is Zero, the number was even.
JZ (jump if Zero) is covered in Section 6.3.
Your turn: Write code that jumps to a label if an integer is negative.

## Slide 16: Applications (5 of 5)
or al,al
jnz IsNotZero ; jump if not zero
Task: Jump to a label if the value in AL is not zero.
Solution: OR the byte with itself, then use the JNZ (jump if not zero) instruction.
ORing any number with itself does not change its value.

## Slide 17: TEST Instruction
Performs a nondestructive AND operation between each pair of matching bits in two operands
No operands are modified, but the Zero flag is affected.
Example: jump to a label if either bit 0 or bit 1 in AL is set.
test al,00000011b
jnz ValueFound
Example: jump to a label if neither bit 0 nor bit 1 in AL is set.
test al,00000011b
jz ValueNotFound

## Slide 18: CMP Instruction (1 of 3)
Compares the destination operand to the source operand
  Nondestructive subtraction of source from destination (destination operand is not changed)
Syntax: CMP destination, source
Example: destination == source
mov al,5
cmp al,5 ; Zero flag set
Example: destination < source
mov al,4
cmp al,5 ; Carry flag set

## Slide 19: CMP Instruction (2 of 3)
Example: destination > source
mov al,6
cmp al,5 ; ZF = 0, CF = 0
(both the Zero and Carry flags are clear)

## Slide 20: CMP Instruction (3 of 3)
Example: destination > source
mov al,5
cmp al,-2 ; Sign flag == Overflow flag
The comparisons shown here are performed with signed integers.
Example: destination < source
mov al,-1
cmp al,5 ; Sign flag != Overflow flag

## Slide 21: What's Next
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Conditional Control Flow Directives

## Slide 22: Conditional Jumps
Jumps Based On . . .
  Specific flags
  Equality
  Unsigned comparisons
  Signed Comparisons
Applications
Encrypting a String
Bit Test (BT) Instruction

## Slide 23: Jcond Instruction
A conditional jump instruction branches to a label when specific register or flag conditions are met
Specific jumps:
  JB, JC - jump to a label if the Carry flag is set
  JE, JZ - jump to a label if the Zero flag is set
  JS - jump to a label if the Sign flag is set
  JNE, JNZ - jump to a label if the Zero flag is clear
  JECXZ - jump to a label if ECX = 0

## Slide 24: Jcond Ranges
Prior to the 386:
  jump must be within –128 to +127 bytes from current location counter
x86 processors:
  32-bit offset permits jump anywhere in memory

## Slide 25: Jumps Based on Specific Flags

## Slide 26: Jumps Based on Equality

## Slide 27: Jumps Based on Unsigned Comparisons

## Slide 28: Jumps Based on Signed Comparisons

## Slide 29: Applications (1 of 5)
cmp eax,ebx
ja Larger
Task: Jump to a label if unsigned EAX is greater than EBX
Solution: Use CMP, followed by JA
cmp eax,ebx
jg Greater
Task: Jump to a label if signed EAX is greater than EBX
Solution: Use CMP, followed by JG

## Slide 30: Applications (2 of 5)
cmp eax,Val1
jbe L1 ; below or equal
Jump to label L1 if unsigned EAX is less than or equal to Val1
cmp eax,Val1
jle L1
Jump to label L1 if signed EAX is less than or equal to Val1

## Slide 31: Applications (3 of 5)
  mov Large,bx
  cmp ax,bx
  jna Next
  mov Large,ax
Next:
Compare unsigned AX to BX, and copy the larger of the two into a variable named Large
  mov Small,ax
  cmp bx,ax
  jnl Next
  mov Small,bx
Next:
Compare signed AX to BX, and copy the smaller of the two into a variable named Small

## Slide 32: Applications (4 of 5)
  cmp WORD PTR [esi],0
  je L1
Jump to label L1 if the memory word pointed to by ESI equals Zero
test DWORD PTR [edi],1
jz L2
Jump to label L2 if the doubleword in memory pointed to by EDI is even

## Slide 33: Applications (5 of 5)
and al,00001011b ; clear unwanted bits
cmp al,00001011b ; check remaining bits
je L1 ; all set? jump to L1
Task: Jump to label L1 if bits 0, 1, and 3 in AL are all set.
Solution: Clear all bits except bits 0, 1,and 3. Then compare the result with 00001011 binary.

## Slide 34: Your turn . . .
Write code that jumps to label L1 if either bit 4, 5, or 6 is set in the BL register.
Write code that jumps to label L1 if bits 4, 5, and 6 are all set in the BL register.
Write code that jumps to label L2 if AL has even parity.
Write code that jumps to label L3 if EAX is negative.
Write code that jumps to label L4 if the expression (EBX – ECX) is greater than zero.

## Slide 35: Encrypting a String
KEY = 70 ; can be any byte value
BUFMAX = 128
.data
buffer BYTE BUFMAX+1 DUP(0)
bufSize DWORD BUFMAX
.code
  mov ecx,bufSize ; loop counter
  mov esi,0 ; index 0 in buffer
L1:
  xor buffer[esi],KEY ; translate a byte
  inc esi ; point to next byte
  loop L1
The following loop uses the XOR instruction to transform every character in a string into a new value.

## Slide 36: String Encryption Program
Tasks:
  Input a message (string) from the user
  Encrypt the message
  Display the encrypted message
  Decrypt the message
  Display the decrypted message
View the Encrypt.asm program's source code. Sample output:
Enter the plain text: Attack at dawn.
Cipher text: «¢¢Äîä-Ä¢-ïÄÿü-Gs
Decrypted: Attack at dawn.

## Slide 37: BT (Bit Test) Instruction
Copies bit n from an operand into the Carry flag
Syntax: BT bitBase, n
  bitBase may be r/m16 or r/m32
  n may be r16, r32, or imm8
Example: jump to label L1 if bit 9 is set in the AX register:
bt AX,9 ; CF = bit 9
jc L1 ; jump if Carry

## Slide 38: What's Next
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Conditional Control Flow Directives

## Slide 39: Conditional Loop Instructions
LOOPZ and LOOPE
LOOPNZ and LOOPNE

## Slide 40: LOOPZ and LOOPE
Syntax:
  LOOPE destination
  LOOPZ destination
Logic:
  ECX  ECX – 1
  if ECX > 0 and ZF=1, jump to destination
Useful when scanning an array for the first element that does not match a given value.
In 32-bit mode, ECX is the loop counter register. In 16-bit real-address mode, CX is the counter, and in 64-bit mode, RCX is the counter.

## Slide 41: LOOPNZ and LOOPNE
LOOPNZ (LOOPNE) is a conditional loop instruction
Syntax:
LOOPNZ destination
LOOPNE destination
Logic:
  ECX  ECX – 1;
  if ECX > 0 and ZF=0, jump to destination
Useful when scanning an array for the first element that matches a given value.

## Slide 42: LOOPNZ Example
.data
array SWORD -3,-6,-1,-10,10,30,40,4
sentinel SWORD 0
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
next:
  test WORD PTR [esi],8000h ; test sign bit
  pushfd ; push flags on stack
  add esi,TYPE array
  popfd ; pop flags from stack
  loopnz next ; continue loop
  jnz quit ; none found
  sub esi,TYPE array ; ESI points to value
quit:
The following code finds the first positive value in an array:

## Slide 43: Your turn . . .
.data
array SWORD 50 DUP(?)
sentinel SWORD 0FFFFh
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
L1: cmp WORD PTR [esi],0 ; check for zero
(fill in your code here)
quit:
Locate the first nonzero value in the array. If none is found, let ESI point to the sentinel value:

## Slide 44: . . . (solution)
.data
array SWORD 50 DUP(?)
sentinel SWORD 0FFFFh
.code
  mov esi,OFFSET array
  mov ecx,LENGTHOF array
L1: cmp WORD PTR [esi],0 ; check for zero
  pushfd ; push flags on stack
  add esi,TYPE array
  popfd ; pop flags from stack
  loope L1 ; continue loop
  jz quit ; none found
  sub esi,TYPE array ; ESI points to value
quit:

## Slide 45: What's Next
Boolean and Comparison Instructions
Conditional Jumps
Conditional Loop Instructions
Conditional Structures
Conditional Control Flow Directives

## Slide 46: Conditional Structures
Block-Structured IF Statements
Compound Expressions with AND
Compound Expressions with OR
WHILE Loops
Table-Driven Selection

## Slide 47: Block-Structured IF Statements
Assembly language programmers can easily translate logical statements written in C++/Java into assembly language. For example:
  mov eax,op1
  cmp eax,op2
  jne L1
  mov X,1
  jmp L2
L1: mov X,2
L2:
if( op1 == op2 )
X = 1;
else
X = 2;

## Slide 48: Your turn . . .
Implement the following pseudocode in assembly language. All values are unsigned:
  cmp ebx,ecx
  ja next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)

## Slide 49: Your turn . . .
Implement the following pseudocode in assembly language. All values are 32-bit signed integers:
  mov eax,var1
  cmp eax,var2
  jle L1
  mov var3,6
  mov var4,7
  jmp L2
L1: mov var3,10
L2:
if( var1 <= var2 )
var3 = 10;
else
{
var3 = 6;
var4 = 7;
}
(There are multiple correct solutions to this problem.)

## Slide 50: Compound Expression with AND (1 of 3)
When implementing the logical AND operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is false, the second expression is skipped:
if (al > bl) AND (bl > cl)
X = 1;

## Slide 51: Compound Expression with AND (2 of 3)
cmp al,bl ; first expression...
ja L1
jmp next
L1:
cmp bl,cl ; second expression...
ja L2
jmp next
L2: ; both are true
mov X,1 ; set X to 1
next:
if (al > bl) AND (bl > cl)
X = 1;
This is one possible implementation . . .

## Slide 52: Compound Expression with AND (3 of 3)
cmp al,bl ; first expression...
jbe next ; quit if false
cmp bl,cl ; second expression...
jbe next ; quit if false
mov X,1 ; both are true
next:
if (al > bl) AND (bl > cl)
X = 1;
But the following implementation uses 29% less code by reversing the first relational operator. We allow the program to "fall through" to the second expression:

## Slide 53: Your turn . . .
Implement the following pseudocode in assembly language. All values are unsigned:
  cmp ebx,ecx
  ja next
  cmp ecx,edx
  jbe next
  mov eax,5
  mov edx,6
next:
if( ebx <= ecx
&& ecx > edx )
{
eax = 5;
edx = 6;
}
(There are multiple correct solutions to this problem.)

## Slide 54: Compound Expression with OR (1 of 2)
When implementing the logical OR operator, consider that HLLs use short-circuit evaluation
In the following example, if the first expression is true, the second expression is skipped:
if (al > bl) OR (bl > cl)
X = 1;

## Slide 55: Compound Expression with OR (2 of 2)
cmp al,bl ; is AL > BL?
ja L1 ; yes
cmp bl,cl ; no: is BL > CL?
jbe next ; no: skip next statement
L1: mov X,1 ; set X to 1
next:
We can use "fall-through" logic to keep the code as short as possible:
if (al > bl) OR (bl > cl)
X = 1;

## Slide 56: WHILE Loops
while( eax < ebx)
eax = eax + 1;
A WHILE loop is really an IF statement followed by the body of the loop, followed by an unconditional jump to the top of the loop. Consider the following example:
top: cmp eax,ebx ; check loop condition
jae next ; false? exit loop
inc eax ; body of loop
jmp top ; repeat the loop
next:
This is a possible implementation:

## Slide 57: Your turn . . .
top: cmp ebx,val1 ; check loop condition
ja next ; false? exit loop
add ebx,5 ; body of loop
dec val1
jmp top ; repeat the loop
next:
while( ebx <= val1)
{
ebx = ebx + 5;
val1 = val1 - 1
}
Implement the following loop, using unsigned 32-bit integers:

## Slide 58: Summary
Bitwise instructions (AND, OR, XOR, NOT, TEST)
  manipulate individual bits in operands
CMP – compares operands using implied subtraction
  sets condition flags
Conditional Jumps & Loops
  equality: JE, JNE
  flag values: JC, JZ, JNC, JP, ...
  signed: JG, JL, JNG, ...
  unsigned: JA, JB, JNA, ...
  LOOPZ, LOOPNZ, LOOPE, LOOPNE
Flowcharts – logic diagramming tool

## Slide 59: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only