## Slide 1: Introduction

## Slide 2: About me
Course Instructors
  Mr. Abdul Qadeer Bilal
  Ms. Ayesha Inam

## Slide 3: Teacher Info.
Name: Abdul Qadeer Bilal
E-mail: a.qadeer@nu.edu.pk
Office #: 2nd Floor. #213
Visiting Hours: (Please Follow it Strictly)
Day | Time
Monday | 10:30 AM to 12:00 PM
Tuesday | 01:30 PM to 03:00 PM
Thursday | 10:30 AM to 12:00 PM

## Slide 4: Course Info.
Code: EE-213
Credit Hours: 3+1
Two lectures per week each of duration 1.5 hour
Lab class each week

## Slide 5: Text Books
Text Books
  Assembly Language for x86 Processors
    by Kip R. Irvine
    6th Edition

## Slide 6: Grading Policy
Class | 
Assignments | 5%
Quizzes | 15%
Midterm Exams | (15+15)%
Class Participation | 5%
Final Exam | 45%
Total | 100%

## Slide 7: Grading Policy
All deadlines will be hard
Re-grading can be requested after grade reporting, within following time limits:
  Midterm: Same day
  Assignments: 2 working days
  Quizzes: 2 working days
  Everything will be final on 3rd day

## Slide 8: General Guidelines
Start work on project/assignment right from the first day
No assignment will be accepted after due date
Assignments copied from others will be marked zero
No excuse will be accepted for a missed assignment or quiz
Unannounced quizzes, so come prepared in the class

## Slide 9: Lecture 01
Week 01

## Slide 10: Chapter Overview
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 11: Welcome to Assembly Language
Some Good Questions to Ask
Assembly Language Applications

## Slide 12: Questions to Ask
Why am I learning Assembly Language?
What background should I have?
What is an assembler?
What hardware/software do I need?
What types of programs will I create?
What do I get with this book?
What will I learn?

## Slide 13: Welcome to Assembly Language (cont)
How does assembly language (AL) relate to machine language?
How do C++ and Java relate to AL?
Is AL portable?
Why learn AL?

## Slide 14: Hierarchy of Computer Languages
Hardware
Machine Language
Assembly Language
High Level Languages
Fortran
C
Pascal

## Slide 15: Assembly Language Applications
Some representative types of applications:
  Business application for single platform
  Hardware device driver
  Business application for multiple platforms
  Embedded systems & computer games

## Slide 16: High Level Language
Called High Level because closer to human language and farther from machine language
Independent of a particular type of processor
Easier to read, write and understand because uses natural language elements
Hides implementation details
Must be translated to machine language

## Slide 17: Assembly Language
Low level programming language
Used to interact with computer hardware
Specific to a particular computer architecture
The instructions in assembly language may directly match the computer’s architecture or they may be translated during execution by a program inside the processor known as a microcode interpreter
Focuses on programming microprocessors
Used to program
  Embedded system
  Device driver programming
  Computer viruses and bootloaders

## Slide 18: Machine Language
Lowest level programming language
Sequence of 1s and 0s
Easily understood by computers
Almost impossible for humans to use
Each CPU has its own unique machine language
Notes: Processors are based on transistors which have just two states, on and off. On state can be represented by 1 and off state can be represented by 0. So basically computers can understand just 1 and 0. The language that we can use to interact with hardware on very low level is called Machine Language.

## Slide 19: Conversion from High Level (HL) to Low Level (LL) Language
From Assembly to Machine Language
  Assembler is used
From High Level to Machine Level Language
  Compiler converts High Level Language to Object Code
  Assembler is used to convert Assembly Language code to Machine Code

## Slide 20: Compiler and Assembler
High Level Language
Assembly Language
Machine Language
Compiler
Assembler
Compiler

## Slide 21: Assembly Language Portability
Can be compiled and run on a wide variety of computers
Assembly is designed for a specific processor family
Motorola 68x00, x86, SUN Sparc, Vax, IBM-370 are different processor architectures

## Slide 22: Conversion from HL to LL Language
Natural Language: Add 5 into 3 and store the result into X
High Level Language: int X = 5 + 3;
Assembly Language:
mov ax, 5
mov bx, 3
add ax, bx
mov X, ax

## Slide 23: Advantages of HL Languages
Program development is faster
  High level statements: fewer instructions to code
Program maintenance is easier
  For the same above reasons
Programs are portable
  Contains less machine dependent details
    Can be used with little or no modifications on different machines
  Compiler translates to the target machine language

## Slide 24: Comparing ASM to High-Level Languages

## Slide 25: What's Next
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 26: Virtual Machine Concept
Virtual Machines
Specific Machine Levels

## Slide 27: Virtual Machines
Tanenbaum: Virtual machine concept
Programming Language analogy:
  Each computer has a native machine language (language L0) that runs directly on its hardware
  A more human-friendly language is usually constructed above machine language, called Language L1
Programs written in L1 can run two different ways:
  Interpretation – L0 program interprets and executes L1 instructions one by one
  Translation – L1 program is completely translated into an L0 program, which then runs on the computer hardware

## Slide 28: Translating Languages
English: Display the sum of A times B plus C.
C++: cout << (A * B + C);
Assembly Language:
mov eax,A
mul B
add eax,C
call WriteInt
Intel Machine Language:
A1 00000000
F7 25 00000004
03 05 00000008
E8 00500000

## Slide 29: Specific Machine Levels
(descriptions of individual levels follow . . . )

## Slide 30: High-Level Language
Level 4
Application-oriented languages
  C++, Java, Pascal, Visual Basic . . .
Programs compile into assembly language (Level 4)

## Slide 31: Assembly Language
Level 3
Instruction mnemonics that have a one-to-one correspondence to machine language
Programs are translated into Instruction Set Architecture Level - machine language (Level 2)

## Slide 32: Instruction Set Architecture (ISA)
Level 2
Also known as conventional machine language
Executed by Level 1 (Digital Logic)

## Slide 33: Digital Logic
Level 1
CPU, constructed from digital logic gates
System bus
Memory
Implemented using bipolar transistors
next: Data Representation

## Slide 34: What's Next
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 35: Data Representation
Binary Numbers
  Translating between binary and decimal
Binary Addition
Integer Storage Sizes
Hexadecimal Integers
  Translating between decimal and hexadecimal
  Hexadecimal subtraction
Signed Integers
  Binary subtraction
Character Storage

## Slide 36: Data Representation
Four basic data representation techniques
  Binary (base 2)
  Octal (base 8)
  Decimal (base 10)
  Hexadecimal (base 16)
System | Base | Possible Digits
Binary | 2 | 0 1
Octal | 8 | 0 1 2 3 4 5 6 7
Decimal | 10 | 0 1 2 3 4 5 6 7 8 9
Hexadecimal | 16 | 0 1 2 3 4 5 6 7 8 9 A B C D E F

## Slide 37: Binary Numbers
Digits are 1 and 0
  1 = true
  0 = false
MSB – most significant bit
LSB – least significant bit
Bit numbering:

## Slide 38: Binary Numbers
Each digit (bit) is either 1 or 0
Each bit represents a power of 2:
Every binary number is a sum of powers of 2

## Slide 39: Translating Binary to Decimal
Weighted positional notation shows how to calculate the decimal value of each binary bit:
dec = (Dn-1  2n-1) + (Dn-2  2n-2) + ... + (D1  21) + (D0  20)
D = binary digit
binary 00001001 = decimal 9:
(1  23) + (1  20) = 9

## Slide 40: Binary to Decimal (1/2)
Weighted Positional Notation method
  D = binary digit
  n = bit position number in binary number
Dec = (Dn-1 x 2n-1) + (Dn-2 x 2n-2) + . . . + (D1 x 21) + (D0 x 20)

## Slide 41: Binary to Decimal (2/2)
0 1 1 12
= (0 x 23) + (1 x 22) + (1 x 21) + (1 x 20)
4-bit number so n = 4
=
D0 = 1
D1 = 1
D2 = 1
D3 = 0
= (D4-1 x 24-1) + (D4-2 x 24-2) + . . . + (D1 x 21) + (D0 x 20)
= (D3 x 23) + (D2 x 22) + . . . + (D1 x 21) + (D0 x 20)
Dec = (Dn-1 x 2n-1) + (Dn-2 x 2n-2) + . . . + (D1 x 21) + (D0 x 20)
7

## Slide 42: Translating Unsigned Decimal to Binary
Repeatedly divide the decimal integer by 2. Each remainder is a binary digit in the translated value:
37 = 100101

## Slide 43: Decimal to Binary (2/2)
Convert 2510 into binary
Division | Quotient | Remainder
25 / 2 | 12 | 1
12 / 2 | 6 | 0
6 / 2 | 3 | 0
3 / 2 | 1 | 1
1 / 2 | 0 | 1
1 1 0 0 12
Final result is 0001 1001
First remainder goes to LSB position
When quotient is 0, remainder goes at MSB position

## Slide 44: Binary Addition
Starting with the LSB, add each pair of digits, include the carry if present.

## Slide 45: Integer Storage Sizes
What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 46: Hexadecimal Integers
Binary values are represented in hexadecimal.

## Slide 47: Hexadecimal to Binary
Each hexadecimal integer corresponds to 4 binary bits
Convert each hexadecimal number to corresponding binary number
0100
1111
1001
0001
4 | F | 9 | 1
0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1

## Slide 48: Translating Binary to Hexadecimal
Each hexadecimal digit corresponds to 4 binary bits.
Example: Translate the binary integer 000101101010011110010100 to hexadecimal:

## Slide 49: Binary to Hexadecimal
Convert each 4 bits of binary into its corresponding hexadecimal
4 | F | 9 | 1
0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 1 | 0 | 0 | 0 | 1
4
F
9
1

## Slide 50: Lecture 02
Week 01

## Slide 51: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only

## Slide 52: Converting Hexadecimal to Decimal
Multiply each digit by its corresponding power of 16:
  dec = (D3  163) + (D2  162) + (D1  161) + (D0  160)
Hex 1234 equals (1  163) + (2  162) + (3  161) + (4  160), or decimal 4,660.
Hex 3BA4 equals (3  163) + (11 * 162) + (10  161) + (4  160), or decimal 15,268.

## Slide 53: Hexadecimal to Decimal (2/2)
3 B A 4
= (3 x 4096) + (11 x 256) + (10 x 16) + (4 x 1)
4-digit number so n = 4
D0 = 4
D1 = A
D2 = B
D3 = 3
= (D4-1 x 164-1) + (D4-2 x 164-2) + (D1 x 161) + (D0 x 160)
= (D3 x 163) + (D2 x 162) + (D1 x 161) + (D0 x 160)
= (12288 + 2816 + 160 + 4) = 15268

## Slide 54: Decimal to Hexadecimal (1/2)
Repeatedly divide the decimal integer by 16 until last quotient is 0
Each remainder is a hex digit
First remainder goes at least significant position and last remainder goes at most significant position

## Slide 55: Powers of 16
Used when calculating hexadecimal values up to 8 digits long:

## Slide 56: Converting Decimal to Hexadecimal
decimal 422 = 1A6 hexadecimal

## Slide 57: Decimal to Hexadecimal (2/2)
Convert 289510 into hexadecimal
Division | Quotient | Remainder
2895 / 16 | 180 | F
180 / 16 | 11 | 4
11 / 16 | 0 | B
B 4 F 16
So 289510 = B 4 F16
First remainder goes to LS position
When quotient is 0, remainder goes at MS position

## Slide 58: Hexadecimal Addition
Divide the sum of two digits by the number base (16). The quotient becomes the carry value, and the remainder is the sum digit.
36 28 28 6A
42 45 58 4B
78 6D 80 B5
1
1
21 / 16 = 1, rem 5
Important skill: Programmers frequently add and subtract the addresses of variables and instructions.

## Slide 59: Hexadecimal Subtraction
When a borrow is required from the digit to the left, add 16 (decimal) to the current digit's value:
C6 75
A2 47
24 2E.
-1
16 + 5 = 21
Practice: The address of var1 is 00400020. The address of the next variable after var1 is 0040006A. How many bytes are used by var1?

## Slide 60: Signed Integers
The highest bit indicates the sign. 1 = negative, 0 = positive
If the highest digit of a hexadecimal integer is > 7, the value is negative. Examples: 8A, C5, A2, 9D

## Slide 61: Signed Integers
Signed integers are either positive or negative
Not possible to stick negative sign to a number in binary numbers
When explicitly mentioned as signed integer, then MSB decides the +ve and –ve sign
In signed binary/octal/hex integers
  MSB = 1  integers is negative
  MSB = 0  integers is positive
Negative integers are represented using 2’s complement notation

## Slide 62: Forming the Two's Complement
Negative numbers are stored in two's complement notation
Represents the additive Inverse
Note that 00000001 + 11111111 = 00000000

## Slide 63: Binary Subtraction
When subtracting A – B, convert B to its two's complement
Add A to (–B)
0 0 0 0 1 1 0 0 0 0 0 0 1 1 0 0
– 0 0 0 0 0 0 1 1 1 1 1 1 1 1 1 0 1
0 0 0 0 1 0 0 1
Practice: Subtract 0101 from 1001.

## Slide 64: Learn How To Do the Following:
Form the two's complement of a hexadecimal integer
Convert signed binary to decimal
Convert signed decimal to binary
Convert signed decimal to hexadecimal
Convert signed hexadecimal to decimal

## Slide 65: Range of Signed Numbers
A certain number of bits can store only a fixed number of signed integers
Bits | Range | Total Numbers
8 | -128 to +127 | 256
16 | -32768 to +32767 | 65,536
32 | -2,147,483,648 to +2,147,483,647 | 4,294,967,296
64 | -9,223,372,036,854,775,808 to +9,223,372,036,854,775,807 | 18,446,744,073,709,551,616

## Slide 66: Range of Unsigned Numbers
Total numbers in signed integers is exactly equal to the total numbers in unsigned integers in the same size of bits
Bits | Range | Total Unsigned Numbers
8 | 0 to 255 | 256
16 | 0 to 65,535 | 65,536
32 | 0 to 4,294,967,295 | 4,294,967,296
64 | 0 to 18,446,744,073,709,551,615 | 18,446,744,073,709,551,616

## Slide 67: 2’s Complement Notation
Useful for processors to perform subtraction with addition operation
A fixed number of bits are used to represent the numbers
The leftmost bit is called sign bit
2’s complement notation is used to represent both +ve and –ve numbers

## Slide 68: How to calculate 2’s complement
How to get 2’s complement of a binary number?
  Take 1’s complement of that number(invert all its bits)
  Add 1 into the inverted binary number
  ... and the result is 2’s complement of that number
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1
+
0 | 1 | 1 | 0 | 1 | 0 | 1 | 0
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1

## Slide 69: 2’s Complement of Hexadecimal
Invert all bits of hex number
All bits of hex numbers can be inverted simply by subtracting the number from F16
Add 1 into the inverted hex number and the result is the 2’s complement
Calculate 2’s complement of (B 4 F)16
4 B 0
4 B 0
1
+
4 B 1
F F F
B 4 F
–
4 B 0

## Slide 70: Converting Signed Binary to Decimal
If MSB is 0, then number is +ve and convert it into decimal in usual way
If MSB is 1, then the number is in 2’s complement notation and follow these steps
  Calculate its 2’s complement again
  Convert this new number into decimal and add a –ve sign with it
As the number was negative
  So in decimal it is
1 | 0 | 0 | 1 | 0 | 1 | 1 | 0
0 | 1 | 1 | 0 | 1 | 0 | 1 | 0
1 0 6
– 1 0 6
2’s comp.
Decimal

## Slide 71: Converting Signed Decimal to Binary
Convert absolute value of decimal into binary
If original decimal number is –ve, calculate 2’s complement of the binary number
Convert -35 to binary
– 35
Absolute Value
35
Binary
0010 0011
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 0
+
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
– 35 = (1101 1101)2
Invert

## Slide 72: Convert Signed Decimal to Hexadecimal
Convert absolute value of decimal to hex
If decimal integer is –ve, create 2’s complement of hexadecimal integer
Convert -2895 to hexadecimal
– 2895
Absolute Value
2895
Hexadecimal
B 4 F
B 4 F
4 B 0
Bit Inversion
Add 1
4 B 1
2’s Complement

## Slide 73: Converting Signed Hex to Decimal (1/3)
In signed hex number, if MSB=1, the number is –ve
To convert it into decimal, follow these steps
  Create its 2’s complement
  Convert the 2’s complemented hex to decimal
  Attach –ve sign to the decimal number

## Slide 74: Converting Signed Hex to Decimal (2/3)
Determine if Signed 8C16 is +ve or –ve
By converting into binary
  If MSB = 1, then number is –ve
  8C16 = (1000 1100)2
  Since MSB = 1, so 8C16 is –ve
Another method
  If leftmost digit > 7, then number is –ve
  Since leftmost digit i.e. 8 > 7
  8C16 is –ve

## Slide 75: Converting Signed Hex to Decimal (3/3)
Convert Signed A316 into decimal
A 3
A > 7 => A3 is –ve
2’s complement of A3 = 5D

## Slide 76: Binary Subtraction
Big advantage of signed number is to use same circuit for addition and subtraction
To perform A – B
  Calculate –B by taking 2’s complement of B
  Perform A+(-B)
0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
-
0 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 1 | 1 | 1 | 0 | 1
0 | 1 | 1 | 1 | 0 | 1 | 1 | 0
+
0 | 1 | 0 | 1 | 0 | 0 | 1 | 1

## Slide 77: Integer Storage System (1/2)
Byte is the basic storage unit in x86 architecture
Byte is composed of 8 bits
8
16
32
64
Byte
Word
Doubleword
Quadword

## Slide 78: Integer Storage System
Some larger measurements units
  One kilobyte = 210 bytes = 1024 bytes
  One megabyte = 220 bytes = 1,048,576 bytes
  One gigabyte = 230 bytes = 1,073,741,824 bytes
  One terabyte = 240 bytes = 1,099,511,627,776 bytes
  One petabyte = 250 bytes = 240 kilobytes
  One exabyte = 260 bytes = 210 petabytes
  One zettabyte = 270 bytes = 230 terabytes
  One yottabyte = 280 bytes = 220 exabytes

## Slide 79: Character Storage
Character sets
  Standard ASCII (0 – 127)
  Extended ASCII (0 – 255)
  ANSI (0 – 255)
  Unicode (0 – 65,535)
Null-terminated String
  Array of characters followed by a null byte
Using the ASCII table
  back inside cover of book

## Slide 80: Numeric Data Representation
pure binary
  can be calculated directly
ASCII binary
  string of digits: "01010101"
ASCII decimal
  string of digits: "65"
ASCII hexadecimal
  string of digits: "9C"
next: Boolean Operations

## Slide 81: What's Next
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 82: Boolean Operations
NOT
AND
OR
Operator Precedence
Truth Tables

## Slide 83: Boolean Algebra
Based on symbolic logic, designed by George Boole
Boolean expressions created from:
  NOT, AND, OR

## Slide 84: NOT
Inverts (reverses) a boolean value
Truth table for Boolean NOT operator:
Digital gate diagram for NOT:

## Slide 85: AND
Truth table for Boolean AND operator:
Digital gate diagram for AND:

## Slide 86: OR
Truth table for Boolean OR operator:
Digital gate diagram for OR:

## Slide 87: Operator Precedence
Examples showing the order of operations:

## Slide 88: Truth Tables (1 of 3)
A Boolean function has one or more Boolean inputs, and returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function
Example: X  Y

## Slide 89: Truth Tables (2 of 3)
Example: X  Y

## Slide 90: Truth Tables (3 of 3)
Example: (Y  S)  (X  S)
Two-input multiplexer

## Slide 91: Summary
Assembly language helps you learn how software is constructed at the lowest levels
Assembly language has a one-to-one relationship with machine language
Each layer in a computer's architecture is an abstraction of a machine
  layers can be hardware or software
Boolean expressions are essential to the design of computer hardware and software

## Slide 92: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only