## Slide 1: Computer Organization & Assembly Language - EE2003

## Slide 2: Lecture ##
Week 14

## Slide 3: Chapter Overview
Disk Storage Systems
File Systems
Disk Directory
Reading and Writing Disk Sectors (7305h)
System-Level File Functions

## Slide 4: Tracks and Sectors
Physical disk geometry - a way of describing the disk’s structure to make it readable by the system BIOS
Track - concentric circle containing data
Sector - part of a track

## Slide 5: Cylinders and Seeking
Cylinder - all tracks readable from one head position
Seek - move read/write heads between tracks

## Slide 6: Disk Formatting
Physical formatting
  aka low-level formatting
  Usually done at the factory.
  Must be done before logical formatting
  Defines the tracks, sectors, and cylinders
Logical formatting
  Permits disk to be accessed using sequentially numbered logical sectors
  Installs a file system (ex: NTFS)
  May install an operating system

## Slide 7: Fragmentation
A fragmented file is one whose sectors are no longer located in contiguous areas of the disk.
  causes read/write heads to skip
  slower file access
  possible read/write errors

## Slide 8: Translation
Translation - conversion of physical disk geometry to a sequence of logical sector numbers
Performed by a hard disk controller (firmware)
Logical sector numbers are numbered sequentially, have no direct mapping to hardware

## Slide 9: Disk Partitions
Logical units that divide a physical hard disk
  Also called volumes
Primary partition
  Up to four permitted
  Each may boot a different OS
Extended partition
  Maximum of one permitted
  May be divided into multiple logical partitions, each with a different drive letter
Primary and Extended
  Up to three primary and one extended

## Slide 10: Logical Partitions
Created from an extended partition
No limit on the number
Each has a separate drive letter
Usually contain data
Can be bootable (ex: Linux)

## Slide 11: Disk Partition Table
Located in the disk's Master Boot Record (MBR), following a block of executable code
Four entries, one for each possible partition
Each entry contains the following fields:
  state (non-active, bootable)
  type of partition (BigDOS, Extended, . . .)
  beginning head, cylinder, & sector numbers
  ending head, cylinder, & sector numbers
  offset of partition from MBR
  number of sectors in the partition

## Slide 12: Cascading Partition Tables
Boot, BigDOS
NA, Extended
NA, BigDOS
NA, BigDOS
Drive D
Drive E
Primary partition
links to
Boot = bootable (system)
NA = non active
BigDOS = over 32 MB
Logical partitions (D, E)
Drive C

## Slide 13: Dual-Boot Example
System 98 and Win2000-A are bootable partitions
  One is called the system partition when active
DATA_1 and BACKUP are logical partitions
  Their data can be shared by both operating systems

## Slide 14: Master Boot Record (MBR)
The MBR contains the following elements:
  Disk partition table
  A program that jumps to the boot sector of the system partition

## Slide 15: File Systems
Directory, File, Cluster Relationships
Clusters
FAT12
FAT16
FAT32
NTFS
Primary Disk Areas

## Slide 16: File System
This is what it does for you:
  Keeps track of allocated and free space
  Maintains directories and filenames
  Tracks the sector location of each file and directory

## Slide 17: Directory, File, Cluster, Sector Relationships

## Slide 18: Cluster (1 of 2)
Smallest unit of space used by a file
Consists of one or more adjacent sectors
Size depends on both the type of file system in use and the disk partition size
A file is a linked sequence of clusters. Example:

## Slide 19: Cluster (2 of 2)
A file always uses at least one cluster
A high percentage of space may be wasted
Example: 8,200-byte file requires three 4K clusters:

## Slide 20: FAT12
Designed for diskettes
Each FAT entry is 12 bits
Very little fault tolerance
  two copies of the FAT (cluster table)
Optimal storage for small files
  512-byte clusters

## Slide 21: FAT16
MS-DOS format for hard disks
16-bit FAT entries
Large cluster size when disk > 1 GB
  inneficient for small files
Max 2 GB size under MS-DOS
Little or no recovery from read/write errors

## Slide 22: FAT32
Supports long filenames
Supported by all version of MS-Windows from Windows 95 onward
  (except Windows NT)
32-bit FAT entries
32 GB maximum volume size
Improved recovery from read/write errors

## Slide 23: NTFS
Supported by Windows NT, 2000, and XP
Handles large volumes
  can span multiple hard drives
Efficient cluster size (4K) on large volumes
Unicode filenames
Permissions on files & folders
Share folders across network
Built-in compression and encryption
Track changes in a change journal
Disk quotas for individuals or groups
Robust error recovery
Disk mirroring

## Slide 24: Primary Disk Areas
A disk or volume is divided into predefined areas and assigned specific logical sectors.
Example: 1.44 MB diskette
  Boot record (sector 0)
  File allocation table (sectors 1 – 18)
  Root directory (sectors 19 – 32)
  Data area (sectors 33 – 2,879)

## Slide 25: Your turn . . .
1. A 1.44 MB diskette has 512 bytes per cluster. Suppose a certain file begins in cluster number 5. Which logical disk sector contains the beginning of the file? (Hint: see page 503).
2. Suppose a certain hard drive has 4 KB per cluster, and we know that the data area begins in sector 100. If a particular file begins in cluster 10, which logical sectors are used by the cluster?
(answers on next panel . . .)

## Slide 26: Answers
1. The data area begins in Sector 33 (see page 503). Each cluster = 1 sector, so the file begins in sector 33 + 5 = sector 38.
2. The hard drive has 8 sectors per cluster. The starting cluster number of the file is 100 + (8 * 10) = 180. Therefore, sectors 180 – 187 are used by the file's first cluster.

## Slide 27: Chapter Overview
Introduction
Keyboard Input with INT 16h
VIDEO Programming with INT 10h
Drawing Graphics Using INT 10h
Memory-Mapped Graphics
Mouse Programming

## Slide 28: Personalities
Bill Gates: co-authored QBASIC interpreter
Gary Kildall: creator of CP/M-86 operating system
  multitasking capabilities
Peter Norton:
  Inside the IBM-PC first book to thoroughly explore IBM-PC software and hardware
  created the Norton Utilities software
Michael Abrash: columnist, expert programmer
  worked on Quake and Doom computer games
  optimized graphics code in Windows NT
  book: The Zen of Code Optimization

## Slide 29: PC-BIOS
The BIOS (Basic Input-Output System) provides low-level hardware drivers for the operating system.
  accessible to 16-bit applications
  written in assembly language, of course
  source code published by IBM in early 1980's
Advantages over MS-DOS:
  permits graphics and color programming
  faster I/O speeds
  read mouse, serial port, parallel port
  low-level disk access

## Slide 30: BIOS Data Area
Fixed-location data area at address 00400h
  this area is also used by MS-DOS
  this area is accessible under Windows 98 & Windows Me, but not under Windows NT, 2000, or XP.
Contents:
  Serial and parallel port addresses
  Hardware list, memory size
  Keyboard status flags, keyboard buffer pointers, keyboard buffer data
  Video hardware configuration
  Timer data

## Slide 31: What's Next
Introduction
Keyboard Input with INT 16h
VIDEO Programming with INT 10h
Drawing Graphics Using INT 10h
Memory-Mapped Graphics
Mouse Programming

## Slide 32: Keyboard Input with INT 16h
How the Keyboard Works
INT 16h Functions

## Slide 33: How the Keyboard Works
Keystroke sends a scan code to the keyboard serial input port
Interrupt triggered: INT 9h service routine executes
Scan code and ASCII code inserted into keyboard typeahead buffer

## Slide 34: Keyboard Flags
16-bits, located at 0040:0017h – 0018h.

## Slide 35: INT 16h Functions
Provide low-level access to the keyboard, more so than MS-DOS.
Input-output cannot be redirected at the command prompt.
Function number is always in the AH register
Important functions:
  set typematic rate
  push key into buffer
  wait for key
  check keyboard buffer
  get keyboard flags

## Slide 36: Function 10h: Wait for Key
.data
scanCode BYTE ?
ASCIICode BYTE ?
.code
mov ah,10h
int 16h
mov scanCode,ah
mov ASCIICode,al
If a key is waiting in the buffer, the function returns it immediately. If no key is waiting, the program pauses (blocks), waiting for user input.

## Slide 37: Function 12h: Get Keyboard Flags
.data
keyFlags WORD ?
.code
mov ah,12h
int 16h
mov keyFlags,ax
Retrieves a copy of the keyboard status flags from the BIOS data area.

## Slide 38: Clearing the Keyboard Buffer
L1: mov ah,11h ; check keyboard buffer
int 16h ; any key pressed?
jz noKey ; no: exit now
mov ah,10h ; yes: remove from buffer
int 16h
cmp ah,scanCode ; was it the exit key?
je quit ; yes: exit now (ZF=1)
jmp L1 ; no: check buffer again
noKey: ; no key pressed
or al,1 ; clear zero flag
quit:
Function 11h clears the Zero flag if a key is waiting in the keyboard typeahead buffer.

## Slide 39: What's Next
Introduction
Keyboard Input with INT 16h
VIDEO Programming with INT 10h
Drawing Graphics Using INT 10h
Memory-Mapped Graphics
Mouse Programming

## Slide 40: VIDEO Programming with INT 10h
Basic Background
Controlling the Color
INT 10h Video Functions
Library Procedure Examples

## Slide 41: Video Modes
Graphics video modes
  draw pixel by pixel
  multiple colors
Text video modes
  character output, using hardware or software-based font table
  mode 3 (color text) is the default
  default range of 80 columns by 25 rows.
  color attribute byte contains foreground and background colors

## Slide 42: Three Levels of Video Access
MS-DOS function calls
  slow, but they work on any MS-DOS machine
  I/O can be redirected
BIOS function calls
  medium-fast, work on nearly all MS-DOS-based machines
  I/O cannot be redirected
Direct memory-mapped video
  fast – works only on 100% IBM-compatible computers
  cannot be redirected
  does not work under Windows NT, 2000, or XP

## Slide 43: Controlling the Color
Mix primary colors: red, yellow, blue
  called subtractive mixing
  add the intensity bit for 4th channel
Examples:
  red + green + blue = light gray (0111)
  intensity + green + blue = white (1111)
  green + blue = cyan (0011)
  red + blue = magenta (0101)
Attribute byte:
  4 MSB bits = background
  4 LSB bits = foreground

## Slide 44: Constructing Attribute Bytes
Color constants defined in Irvine32.inc and Irvine16.inc:
Examples:
  Light gray text on a blue background:
    (blue SHL 4) OR lightGray
  White text on a red background:
    (red SHL 4) OR white

## Slide 45: INT 10h Video Functions
AH register contains the function number
00h: Set video mode
  text modes listed in Table 15-5
  graphics modes listed in Table 15-6
01h: Set cursor lines
02h: Set cursor position
03h: Get cursor position and size
06h: Scroll window up
07h: Scroll window down
08h: Read character and attribute

## Slide 46: INT 10h Video Functions (cont)
09h: Write character and attribute
0Ah: Write character
10h (AL = 03h): Toggle blinking/intensity bit
0Fh: Get video mode
13h: Write string in teletype mode

## Slide 47: Displaying a Color String
Write one character and attribute:
  mov si,OFFSET string
  . . .
  mov ah,9 ; write character/attribute
  mov al,[si] ; character to display
  mov bh,0 ; video page 0
  mov bl,color ; attribute
  or bl,10000000b ; set blink/intensity bit
  mov cx,1 ; display it one time
  int 10h

## Slide 48: Gotoxy Procedure
;--------------------------------------------------
Gotoxy PROC
;
; Sets the cursor position on video page 0.
; Receives: DH,DL = row, column
; Returns: nothing
;---------------------------------------------------
pusha
mov ah,2
mov bh,0
int 10h
popa
ret
Gotoxy ENDP

## Slide 49: Clrscr Procedure
Clrscr PROC
pusha
mov ax,0600h ; scroll window up
mov cx,0 ; upper left corner (0,0)
mov dx,184Fh ; lower right corner (24,79)
mov bh,7 ; normal attribute
int 10h ; call BIOS
mov ah,2 ; locate cursor at 0,0
mov bh,0 ; video page 0
mov dx,0 ; row 0, column 0
int 10h
popa
ret
Clrscr ENDP

## Slide 50: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only