## Slide 1: Computer Organization & Assembly Language - EE2003

## Slide 2: Lecture 03
Week 02

## Slide 3: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 4: General Concepts
Basic microcomputer design
Instruction execution cycle
Reading from memory
How programs run

## Slide 5: Organization and Architecture
Computer Architecture
  Attributes of a computer that have a direct impact on the logical program execution
  e.g. I/O mechanisms, memory addressing techniques
Computer Organization
  Operational units and their interconnection that realizes the architectural specifications
  e.g. control signals, interconnection between computer and its peripherals

## Slide 6: Basic Computer Organization (1/2)
Computer has 3 main components
  Processor, also called Central Processing Unit (CPU)
  Memory and Storage Devices
  I/O Devices
These components communicate with each other through
  Data Bus
  I/O Bus
  Address Bus
  Control Bus

## Slide 7: Basic Computer Organization (2/2)
Memory Storage Unit
I/O Device #1
I/O Device #2
Central
Processing Unit
(CPU)
ALU | CU | CLOCK
I/O Bus
Address Bus
Control Bus
Registers
Data Bus

## Slide 8: Basic Microcomputer Design
clock synchronizes CPU operations
control unit (CU) coordinates sequence of execution steps
ALU performs arithmetic and bitwise processing

## Slide 9: Central Processing Unit (CPU)
Generally called Processor
Contains
  Clock
  Registers
  Arithmetic Logic Unit (ALU)
    Performs arithmetic and logic instructions
  Control Unit (CU)
    Generates the control signals required to execute the instructions

## Slide 10: Clock (1/3)
Clock cycle is basic unit of time for machine instructions
Synchronizes Processor and Bus operations
Clock cycle = Clock period = 1/(Clock Rate)
Clock Rate = Clock Frequency = Cycles per sec
  1 Hz clock produces 1 Clock Cycle in 1 second
  1 KHz clock produces 1000 Clock Cycles in 1 second
  1 MHz clock produces 1,000,000 cycles in 1 second
  1 GHz clock produces 1,000,000,000 cycles in 1 second

## Slide 11: Clock (2/3)
Clock Frequency | Clock Period (sec) | Time to execute one instruction
1 Hz | 1 | 1 sec
1 KHz | 0.001 | 1 ms (millisecond)
1 MHz | 0.000,001 | 1 μs (microsecond)
1 GHz | 0.000,000,001 | 1 ns (nanosecond)
1
0
One Cycle

## Slide 12: Clock (2/3)
synchronizes all CPU and BUS operations
machine (clock) cycle measures time of a single operation
clock is used to trigger events

## Slide 13: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 14: Memory (1/2)
Ordered sequence of bytes
  Sequence number is called memory address
Byte addressable memory
  Each byte has a unique address
Physical address space
  Determined by the address bus width
  Pentium has 32-bit address bus
    Physical address space of Pentium = 232 bytes = 4 GB
  Itanium with 64-bit address bus can support up to 264 bytes of physical address space

## Slide 15: Memory (2/2)
Address of location to be read/written is placed on the address bus
Data to be read/written is placed on the data bus by memory/processor
Two control signals read and write decide the reading or writing operations
Memory Unit
Address
Read
Write
Data

## Slide 16: Physical Address Space
Address space is the set of addressable memory locations (bytes)
Address
in decimal
Address
in hex
0
1
2
232-1
00000000
00000001
00000002
FFFFFFFD
FFFFFFFE
FFFFFFFF

## Slide 17: Reading from Memory
Multiple clock cycles are required
Memory responds much more slowly than CPU
Reading process is carried out in this way
  Address is placed on the address bus
  Read Line (RD) goes low indicating that processor wants to read
  CPU waits for memory to respond
  Read Line (RD) goes high indicating that data has been placed on the data bus

## Slide 18: Memory Read and Write Cycles
In Read Cycle, the Processor
  places address on address bus
  asserts the memory read control signal
  waits for memory to place data on the data bus
  reads the data from data bus
  drops the memory read signal
In Write Cycle, the Processor
  places address on the address bus
  asserts the memory write control signal
  places the data on the data bus
  waits for memory to store the data
  drops the memory write signal

## Slide 19: Reading from Memory

## Slide 20: Memory Hierarchy
Registers
  Fastest storage elements
Cache Memory
  Stores recently used instructions
Main Memory
Magnetic Disk
  Stores data permanently
Magnetic Tape
Magnetic Tape
Magnetic Disk
CD-ROM
CD-RW
DVD-RW
Off-line Storage
Outboard
Storage
Inboard
Storage
Main Memory
Cache
Regis-ters
Lower cost per Byte
Higher Speed, Smaller Size

## Slide 21: Cache Memory
High-speed expensive static RAM both inside and outside the CPU.
  Level-1 cache: inside the CPU
  Level-2 cache: outside the CPU
Cache hit: when data to be read is already in cache memory
Cache miss: when data to be read is not in cache memory.

## Slide 22: How a Program Runs

## Slide 23: Multitasking
OS can run multiple programs at the same time.
Multiple threads of execution within the same program.
Scheduler utility assigns a given amount of CPU time to each running program.
Rapid switching of tasks
  gives illusion that all programs are running at once
  the processor must support task switching.

## Slide 24: IA-32 Processor Architecture
Modes of operation
Basic execution environment
Floating-point unit
Intel Microprocessor history

## Slide 25: Basic Execution Environment
Addressable memory
General-purpose registers
Index and base registers
Specialized register uses
Status flags
Floating-point, MMX, XMM registers

## Slide 26: Registers
Very high speed memory units inside CPU
Can be categorized into
  General Purpose Registers
  Segment Registers
  Instruction Pointer
  EFLAGS Register
    Control Flags
    Status Flags

## Slide 27: General Purpose Registers
Used primarily for arithmetic and data movement
Eight 32-bit Extended general purpose registers
Register | Description | Specialized Usage
EAX | Accumulator | Used in mul and div instruction
EBX | Base | 
ECX | Counter | Used in LOOP instruction
EDX | Data | 
EBP | Base Pointer | Used to reference local variables on stack
ESP | Stack Pointer | Points at top of the stack, used by PUSH and POP
ESI | Source Index | Used by high speed memory transfer instruction
EDI | Destination Index | Used by high speed memory transfer instruction

## Slide 28: Accessing Parts of Registers (1/2)
Portions of General Purpose Registers can also be accessed
  Lower 16 bits of EAX are named AX
  AX can further be divided into
    AL = Lower 8 bits
    AH = Higher 8 bits
EAX
AX
AH
AL
32 bits
16 bits
8 bits
0
7
8
15
16
31
8 bits

## Slide 29: Accessing Parts of Registers (2/2)
  EAX, EBX, ECX, EDX can be accessed at word and byte level
  EBP, ESP, ESI, EDI can be accessed at word level
32-bit | 16-bit | 8-bit Higher | 8-bit Lower
EAX | AX | AH | AL
EBX | BX | BH | BL
ECX | CX | CH | CL
EDX | DX | DH | DL
32-bit | 16-bit Lower
ESP | SP
EBP | BP
ESI | SI
EDI | DI

## Slide 30: Segment Registers (1/2)
Six 16-bit segment registers
Indicate base addresses of pre-assigned memory areas
An assembly program usually contains 3 segments
  Stack Segment: holds local function variables and function parameters
  Data Segment: holds variables
  Code Segment: holds program instructions

## Slide 31: Segment Registers (2/2)
SS = Stack Segment
DS = Data Segment
CS = Code Segment
3 extra segment registers
  ES, FS, GS (Extra Segment)
SS
DS
CS
ES
FS
GS

## Slide 32: Instruction Pointer
Represented by EIP
Also called Program Counter (PC)
Contains the address of next instruction to be executed
Its value changes with the execution of program
Certain machine instructions influence the value of EIP

## Slide 33: Status Flags (1/2)
EFLAGS register consists of individual binary bits
Can be categorized into
  Control Flags: control the operation of CPU
  Status Flags: reflect the outcome of arithmetic and logical operations
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | ID | VIP | VIF | AC | VM | RF | 0 | NT | IOPL | OF | DF | IF | TF | SF | ZF | 0 | AF | 0 | PF | 1 | CF

## Slide 34: Status Flags (2/2)
Arithmetic and Logical operations set/reset them
Status Flags are
  Carry Flag (CF): set when unsigned arithmetic operation produces a carry
  Overflow Flag (OF): sets when signed arithmetic result is out of range
  Sign Flag (SF): sets when result of operation is –ve
  Zero Flag (ZF): sets when result of operation is zero
  Auxiliary Flag (AF): sets when there is a carry from bit 3 to bit 4
  Parity Flag (PF): sets when parity is even

## Slide 35: Floating Point Unit (FPU)
FPU performs high speed floating point operations
Integrated into main processor chip from Intel486 onward
Eight 80-bit floating point data registers
All arranged as a stack
ST(7)
ST(1)
ST(0)
ST(3)
ST(2)
ST(5)
ST(4)
ST(6)

## Slide 36: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only

## Slide 37: Lecture 04
Week 02

## Slide 38: Instruction Execution Cycle
Fetch
Decode
Fetch operands
Execute
Store output

## Slide 39: Instruction Execution Cycle (1/2)
A program is loaded into memory before execution
Instruction Pointer (IP) contains the address of next instruction to be executed
Instruction Queue contains the group of instructions about to be executed
Three basic steps in execution of a machine instruction
  Fetch
  Decode
  Execute
Two more steps if the instruction uses an operand located in memory
  Fetch Operand
  Store Output

## Slide 40: Instruction Execution Cycle (2/2)
Order of steps when instruction uses an operand located in memory
  Instruction Fetch (IF)
  Instruction Decode (ID)
  Operand Fetch from Memory (OF)
  Instruction Execute (IE)
  Write Back in Memory (WB)
Instruction Execution Cycle (IEC) is the combination of all above operations

## Slide 41: Instruction Fetch
Program Counter (PC) or IP holds address of next instruction to be executed
Processor fetches instruction from memory pointed to be PC
Increment PC to the next instruction
Fetching operation concludes here

## Slide 42: Instruction Decode
Control Unit (CU) determines the function of the instruction
Instruction’s input operands are passed to ALU
Signals sent to ALU to perform the desired operation

## Slide 43: Operand Fetch from Memory
Sometimes instructions may involve some operands located in memory
In this case, data should be retrieved from memory
The CU uses a memory read operation
CU copies these operands into Instruction Registers which are invisible to user programs

## Slide 44: Instruction Execute
The instruction is ready for execution at this stage
ALU executes the instruction
ALU updates the status flags providing information about the result

## Slide 45: Write Back in Memory
The output may be required to save in memory for future uses
CU performs a write operation to save this output into memory

## Slide 46: IEC Graphical View
Instruction Fetch
Instruction Decode
Operand Fetch
Instruction Execute
Write Back in Memory
Obtain instruction from Instruction Queue
Determine required action to be executed
Locate and obtain operand from memory location
Compute the required operation
Deposit results in the storage for future use
Infinite Cycle

## Slide 47: Intel Microprocessor History
Intel 8086, 80286
IA-32 processor family
P6 processor family
CISC and RISC

## Slide 48: Early Intel Microprocessors
Intel 8080
  64K addressable RAM
  8-bit registers
  CP/M operating system
  S-100 BUS architecture
  8-inch floppy disks!
Intel 8086/8088
  IBM-PC Used 8088
  1 MB addressable RAM
  16-bit registers
  16-bit data bus (8-bit for 8088)
  separate floating-point unit (8087)

## Slide 49: The IBM-AT
Intel 80286
  16 MB addressable RAM
  Protected memory
  several times faster than 8086
  introduced IDE bus architecture
  80287 floating point unit

## Slide 50: Intel IA-32 Family
Intel386
  4 GB addressable RAM, 32-bit registers, paging (virtual memory)
Intel486
  instruction pipelining
Pentium
  superscalar, 32-bit address bus, 64-bit internal data path

## Slide 51: 64-bit Processors
Intel64
  64-bit linear address space
  Intel: Pentium Extreme, Xeon, Celeron D, Pendium D, Core 2, and Core i7
IA-32e Mode
  Compatibility mode for legacy 16- and 32-bit applications
  64-bit Mode uses 64-bit addresses and operands

## Slide 52: Intel Technologies
HyperThreading technology
  two tasks execute on a single processor at the same time
Dual Core processing
  multiple processor cores in the same IC package
  each processor has its own resources and communication path with the bus

## Slide 53: Intel Processor Families
Currently Used:
Pentium & Celeron – dual core
Core 2 Duo - 2 processor cores
Core 2 Quad - 4 processor cores
Core i7 – 4 processor cores

## Slide 54: CISC and RISC
CISC – complex instruction set
  large instruction set
  high-level operations
  requires microcode interpreter
  examples: Intel 80x86 family
RISC – reduced instruction set
  simple, atomic instructions
  small instruction set
  directly executed by hardware
  examples:
    ARM (Advanced RISC Machines)
    DEC Alpha (now Compaq)

## Slide 55: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 56: Modes of Operation
Protected mode
  native mode (Windows, Linux)
Real-address mode
  native MS-DOS
System management mode
  power management, system security, diagnostics
Virtual-8086 mode
  hybrid of Protected
  each program has its own 8086 computer

## Slide 57: Addressable Memory
Protected mode
  4 GB
  32-bit address
Real-address and Virtual-8086 modes
  1 MB space
  20-bit address

## Slide 58: IA-32 Memory Management
Real-address mode
Calculating linear addresses
Protected mode
Multi-segment model
Paging

## Slide 59: x86 Operation Modes
x86 architecture operates in 3 basic different modes
  Protected Mode
    All instructions and features of processor are available
    Programs cannot reference memory outside their segments
    Virtual-8086 is special mode of Protected Mode
  Real-Address Mode
    Programs can have direct access to memory and hardware devices
    … so operating system can crash in this mode
  System Management Mode
    Implemented in processors customized for a particular system setup
    Supports power management and system security

## Slide 60: x86 Memory Management
Memory is managed according to the operation mode
  Real-Address Mode
  Protected Mode

## Slide 61: Real-Address Mode Memory Management
16-bit registers
20-bit address bus
  Physical Address Space = 1MByte
  Linear or Absolute Address range is 00000h to FFFFFh
How 20-bit address can be accommodated in 16-bit Registers?
  Solution lies in Segmented Memory

## Slide 62: Real-Address Mode Memory Management
Programs cannot use linear address directly because of 16-bit registers
Addresses are represented using 2 16-bit registers
  One 16-bit value is called Segment Value which is placed in segment register
  Other 16-bit value is called Offset value

## Slide 63: Segmented Memory Scheme
All memory is divided in 64KBytes segments
Each segment begins at an address having a zero in its last hex digit
  … this zero is omitted when representing segment value in 16-bit registers
    A segment value of E00016 refers to the segment address of E000016
If we have Physical Address Space of 220 bytes, and size of each segment is 64KBytes (216bytes), how many segments do we have?

## Slide 64: Segmented Memory Map
64 KBytes
00000
10000
20000
30000
40000
50000
7000:0000
7000:FFFF
Segment
Offset
017A
7000:017A
F0000
64 KBytes
60000
70000
80000
90000
A0000
B0000
C0000
D0000
E0000
Segment
Offset
7000:017A is called Logical Address
7017A is called Linear/Absolute Address

## Slide 65: Calculating Linear Addresses
Given a segment address, multiply it by 16 (add a hexadecimal zero), and add it to the offset
Example: convert 08F1:0100 to a linear address
Adjusted Segment value: 0 8 F 1 0
Add the offset: 0 1 0 0
Linear address: 0 9 0 1 0

## Slide 66: 20-bit Linear Address Calculation
Segment value
0
15
Offset value
X
1016
+
20-bit Linear Address in hex
In Hex
In Hex
0
15
How to convert a 16-bitSeg:16-bitOffset logical address into 20-bit linear/absolute address

## Slide 67: Protected Mode Memory Management
Restricts application programs from accessing system hardware
Logical Address consists of
  16-bit segment selector (Segment Registers)
  32-bit offset value
Program’s linear address space is 4GBytes
  What is address bus width?
A typical protected-mode program has three segments
  Code Segment
  Data Segment
  Stack Segment
Segment Registers point to the Segment Descriptor Table
  … Segment Descriptor Tables are created by OS to keep track of individual program segments

## Slide 68: Your turn . . .
What linear address corresponds to the segment/offset address 028F:0030?
028F0 + 0030 = 02920
Always use hexadecimal notation for addresses.

## Slide 69: Your turn . . .
What segment addresses correspond to the linear address 28F30h?
Many different segment-offset addresses can produce the linear address 28F30h. For example:
28F0:0030, 28F3:0000, 28B0:0430, . . .

## Slide 70: Flat Segment Model
Single global descriptor table (GDT).
All segments mapped to entire 32-bit address space

## Slide 71: Multi-Segment Model
Each program has a local descriptor table (LDT)
  holds descriptor for each segment used by the program

## Slide 72: Paging
Paging divides the linear address space into fixed-sized block called pages
IA-32 uses pages of size 4 KB
Pages are allocated space on main memory
  … if main memory is full, then on hard disk
Complete set of pages mapped by OS is called Virtual Memory

## Slide 73: Paging
We want to run many programs in parallel
Main memory may not be enough to load all of them at the same time
Disk storage is cheaper and we have plenty of it
Paging gives an illusion that we have unlimited main memory
The more a program depends on paging, the slower it runs
Higher amount of main memory means less usage of paging

## Slide 74: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 75: Components of an IA-32 Microcomputer
Motherboard
Video output
Memory
Input-output ports

## Slide 76: Motherboard
CPU socket
External cache memory slots
Main memory slots
BIOS chips
Sound synthesizer chip (optional)
Video controller chip (optional)
IDE, parallel, serial, USB, video, keyboard, joystick, network, and mouse connectors
PCI bus connectors (expansion cards)

## Slide 77: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 78: Intel 965 Express Chipset

## Slide 79: Video Output
Video controller
  on motherboard, or on expansion card
  AGP (accelerated graphics port technology)*
Video memory (VRAM)
Video CRT Display
  uses raster scanning
  horizontal retrace
  vertical retrace
Direct digital LCD monitors
  no raster scanning required

## Slide 80: Sample Video Controller (ATI Corp.)
  128-bit 3D graphics performance powered by RAGE™ 128 PRO
  3D graphics performance
  Intelligent TV-Tuner with Digital VCR
  TV-ON-DEMAND™
  Interactive Program Guide
  Still image and MPEG-2 motion video capture
  Video editing
  Hardware DVD video playback
  Video output to TV or VCR

## Slide 81: Memory
ROM
  read-only memory
EPROM
  erasable programmable read-only memory
Dynamic RAM (DRAM)
  inexpensive; must be refreshed constantly
Static RAM (SRAM)
  expensive; used for cache memory; no refresh required
Video RAM (VRAM)
  dual ported; optimized for constant video refresh
CMOS RAM
  complimentary metal-oxide semiconductor
  system setup information
See: Intel platform memory (Intel technology brief: link address may change)

## Slide 82: Input-Output Ports
USB (universal serial bus)
  intelligent high-speed connection to devices
  up to 12 megabits/second
  USB hub connects multiple devices
  enumeration: computer queries devices
  supports hot connections
Parallel
  short cable, high speed
  common for printers
  bidirectional, parallel data transfer
  Intel 8255 controller chip

## Slide 83: Input-Output Ports (cont)
Serial
  RS-232 serial port
  one bit at a time
  uses long cables and modems
  16550 UART (universal asynchronous receiver transmitter)
  programmable in assembly language

## Slide 84: Device Interfaces
ATA host adapters
  intelligent drive electronics (hard drive, CDROM)
SATA (Serial ATA)
  inexpensive, fast, bidirectional
FireWire
  high speed (800 MB/sec), many devices at once
Bluetooth
  small amounts of data, short distances, low power usage
Wi-Fi (wireless Ethernet)
  IEEE 802.11 standard, faster than Bluetooth

## Slide 85: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 86: Levels of Input-Output
Level 3: High-level language function
  examples: C++, Java
  portable, convenient, not always the fastest
Level 2: Operating system
  Application Programming Interface (API)
  extended capabilities, lots of details to master
Level 1: BIOS
  drivers that communicate directly with devices
  OS security may prevent application-level code from working at this level

## Slide 87: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 88: Programming levels
Assembly language programs can perform input-output at each of the following levels:

## Slide 89: Summary
Central Processing Unit (CPU)
Arithmetic Logic Unit (ALU)
Instruction execution cycle
Multitasking
Floating Point Unit (FPU)
Complex Instruction Set
Real mode and Protected mode
Motherboard components
Memory types
Input/Output and access levels

## Slide 90: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only