## Slide 1: Computer Organization & Assembly Language - EE2003

## Slide 2: Lecture 05
Week 03

## Slide 3: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 4: Chapter Overview
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 5: Basic Elements of Assembly Language
Integer constants
Integer expressions
Character and string constants
Reserved words and identifiers
Directives and instructions
Labels
Mnemonics and Operands
Comments
Examples

## Slide 6: Integer Constants
Optional leading + or – sign
binary, decimal, hexadecimal, or octal digits
Common radix characters:
  h – hexadecimal
  d – decimal
  b – binary
  r – encoded real
Examples: 30d, 6Ah, 42, 1101b
Hexadecimal beginning with letter: 0A5h

## Slide 7: Integer Expressions
Operators and precedence levels:
Examples:

## Slide 8: Character and String Constants
Enclose character in single or double quotes
  'A', "x"
  ASCII character = 1 byte
Enclose strings in single or double quotes
  "ABC"
  'xyz'
  Each character occupies a single byte
Embedded quotes:
  'Say "Goodnight," Gracie'

## Slide 9: Reserved Words and Identifiers
Reserved words cannot be used as identifiers
  Instruction mnemonics, directives, type attributes, operators, predefined symbols
  See MASM reference in Appendix A
Identifiers
  1-247 characters, including digits
  not case sensitive
  first character must be a letter, _, @, ?, or $

## Slide 10: Reserved Words
Have special meaning and can only be used in correct context
  Instruction mnemonics like MOV, ADD, SUB, INT etc.
  Register Names like AX, BX, DL, DH etc.
  Directives like .DATA, .CODE etc.
  Attributes like BYTE, WORD etc.
  Operators used in constant expressions
  Predefined symbols

## Slide 11: Identifiers
Name of a variable, constant, procedure or a code label selected by programmer
Some rules to follow while choosing identifier names
  From 1 to 247 number of characters
  Names are not case sensitive
  An identifier cannot be the same as an assembler reserved word
  First character must be a letter (a-z, A-Z), underscore(_), @, ? Or $. Subsequent characters may also contain digits
Examples are var1, CounT, _name, _1344

## Slide 12: Directives
Commands that are recognized and acted upon by the assembler
  Not part of the Intel instruction set
  Used to declare code, data areas, select memory model, declare procedures, etc.
  not case sensitive
Different assemblers have different directives
  NASM not the same as MASM, for example

## Slide 13: Instructions
Assembled into machine code by assembler
Executed at runtime by the CPU
We use the Intel IA-32 instruction set
An instruction contains:
  Label (optional)
  Mnemonic (required)
  Operand (depends on the instruction)
  Comment (optional)

## Slide 14: Instructions
A statement that becomes executable when a program is assembled
Translated by assembler into machine language
An Instruction contains four basic parts
  Label (optional)
  Instruction Mnemonic (required)
  Operand(s) (usually required)
  Comment (optional)
Basic syntax is
[label:] mnemonic [operand] [;comment]

## Slide 15: Labels
Act as place markers
  marks the address (offset) of code and data
Follow identifer rules
Data label
  must be unique
  example: myArray (not followed by colon)
Code label
  target of jump and loop instructions
  example: L1: (followed by colon)

## Slide 16: Mnemonics and Operands
Instruction Mnemonics
  memory aid
  examples: MOV, ADD, SUB, MUL, INC, DEC
Operands
  constant
  constant expression
  register
  memory (data label)
Constants and constant expressions are often called immediate values

## Slide 17: Comments
Comments are good!
  explain the program's purpose
  when it was written, and by whom
  revision information
  tricky coding techniques
  application-specific explanations
Single-line comments
  begin with semicolon (;)
Multi-line comments
  begin with COMMENT directive and a programmer-chosen character
  end with the same programmer-chosen character

## Slide 18: NOP (No Operation) Instruction
The safest and even most useless instruction in assembly language
Does not do anything except occupying 1 byte of program storage
Sometimes used by assemblers to align code to even-address boundaries
00000000 66 8B C3 MOV AX, BX
00000003 90 NOP
00000004 8B D1 MOV EDX, ECX

## Slide 19: Instruction Format Examples
No operands
  stc ; set Carry flag
One operand
  inc eax ; register
  inc myByte ; memory
Two operands
  add ebx,ecx ; register, register
  sub myByte,25 ; memory, constant
  add eax,36 * 25 ; register, constant-expression

## Slide 20: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 21: Example: Adding and Subtracting Integers
TITLE Add and Subtract (AddSub.asm)
; This program adds and subtracts 32-bit integers.
INCLUDE Irvine32.inc
.code
main PROC
mov eax,10000h ; EAX = 10000h
add eax,40000h ; EAX = 50000h
sub eax,20000h ; EAX = 30000h
call DumpRegs ; display registers
exit
main ENDP
END main

## Slide 22: Example Output
Program output, showing registers and flags:
EAX=00030000 EBX=7FFDF000 ECX=00000101 EDX=FFFFFFFF
ESI=00000000 EDI=00000000 EBP=0012FFF0 ESP=0012FFC4
EIP=00401024 EFL=00000206 CF=0 SF=0 ZF=0 OF=0

## Slide 23: Suggested Coding Standards (1 of 2)
Some approaches to capitalization
  capitalize nothing
  capitalize everything
  capitalize all reserved words, including instruction mnemonics and register names
  capitalize only directives and operators
Other suggestions
  descriptive identifier names
  spaces surrounding arithmetic operators
  blank lines between procedures

## Slide 24: Suggested Coding Standards (2 of 2)
Indentation and spacing
  code and data labels – no indentation
  executable instructions – indent 4-5 spaces
  comments: right side of page, aligned vertically
  1-3 spaces between instruction and its operands
    ex: mov ax,bx
  1-2 blank lines between procedures

## Slide 25: Alternative Version of AddSub
TITLE Add and Subtract (AddSubAlt.asm)
; This program adds and subtracts 32-bit integers.
.386
.MODEL flat,stdcall
.STACK 4096
ExitProcess PROTO, dwExitCode:DWORD
DumpRegs PROTO
.code
main PROC
mov eax,10000h ; EAX = 10000h
add eax,40000h ; EAX = 50000h
sub eax,20000h ; EAX = 30000h
call DumpRegs
INVOKE ExitProcess,0
main ENDP
END main

## Slide 26: Program Template
TITLE Program Template (Template.asm)
; Program Description:
; Author:
; Creation Date:
; Revisions:
; Date: Modified by:
INCLUDE Irvine32.inc
.data
; (insert variables here)
.code
main PROC
; (insert executable instructions here)
exit
main ENDP
; (insert additional procedures here)
END main

## Slide 27: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 28: Assembling, Linking, and Running Programs
Assemble-Link-Execute Cycle
Listing File
Map File

## Slide 29: Assemble-Link Execute Cycle
The following diagram describes the steps from creating a source program through executing the compiled program.
If the source code is modified, Steps 2 through 4 must be repeated.

## Slide 30: Assemble-Link-Debug Cycle (2/3)
Editor
  Write new (.asm) programs
  Make changes to existing ones
Assembler
  Translate (.asm) file into object (.obj) file in machine language
  Can produce a listing (.lst) file that shows the work of assembler
Linker
  Combine object (.obj) files with link library (.lib) files
  Produce executable (.exe) file
  Can produce optional (.map) file
Edit
Assemble
Link
Run
prog.asm
prog.obj
prog.lst
prog.exe
prog.map
library.lib
Debug

## Slide 31: Assemble-Link-Debug Cycle (3/3)
Debugger
  Trace program execution
    Either step-by-step, or
    Use breakpoints
  View
    Source (.asm) code
    Registers
    Memory by name & by address
    Modify register & memory content
  Discover errors and go back to the editor to fix the program bugs
Edit
Assemble
Link
Run
prog.asm
prog.obj
prog.lst
prog.exe
prog.map
library.lib
Debug

## Slide 32: Listing File
Use it to see how your program is compiled
Contains
  source code
  addresses
  object code (machine language)
  segment names
  symbols (variables, procedures, and constants)
Example: addSub.lst

## Slide 33: Listing File
Use it to see how your program is assembled
Contains
  Source code
  Object code
  Relative addresses
  Segment names
  Symbols
    Variables
    Procedures
    Constants
Object & source code in a listing file
00000000 .code
00000000 main PROC
00000000 B8 00060000 mov eax, 60000h
00000005 05 00080000 add eax, 80000h
0000000A 2D 00020000 sub eax, 20000h
0000000F 6A 00 push 0
00000011 E8 00000000 E call ExitProcess
00000016 main ENDP
END main
object code
(hexadecimal)
source code
Relative
Addresses

## Slide 34: Map File
Information about each program segment:
  starting address
  ending address
  size
  segment type
Example: addSub.map (16-bit version)

## Slide 35: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only

## Slide 36: Lecture 06
Week 03

## Slide 37: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 38: Defining Data
Intrinsic Data Types
Data Definition Statement
Defining BYTE and SBYTE Data
Defining WORD and SWORD Data
Defining DWORD and SDWORD Data
Defining QWORD Data
Defining TBYTE Data
Defining Real Number Data
Little Endian Order
Adding Variables to the AddSub Program
Declaring Uninitialized Data

## Slide 39: Intrinsic Data Types (1 of 2)
BYTE, SBYTE
  8-bit unsigned integer; 8-bit signed integer
WORD, SWORD
  16-bit unsigned & signed integer
DWORD, SDWORD
  32-bit unsigned & signed integer
QWORD
  64-bit integer
TBYTE
  80-bit integer

## Slide 40: Intrinsic Data Types (2 of 2)
REAL4
  4-byte IEEE short real
REAL8
  8-byte IEEE long real
REAL10
  10-byte IEEE extended real

## Slide 41: Data Definition Statement (1/2)
Assigns storage in memory for a variable
Syntax for a data definition statement is
Name is optional and must follow the rules of naming the identifiers
At least one initializer is required
Question mark (?) can be used as initializer if uninitialized variable
[name] directive initializer [,initializer]

## Slide 42: Data Definition Statement (2/2)
Directive can be any of the following
Directive | Description | Usage
DB | Define Byte | 8-bit Integer
DW | Define Word | 16-bit Integer
DD | Define Doubleword | 32-bit Integer
DQ | Define Quadword | 64-bit Integer
DT | Define Tenbytes | 80-bit Integer

## Slide 43: DB Directive
Defines an 8-bit signed or unsigned variable
The initializer must fit into 8-bits either signed or unsigned
name shows the offset from the beginning of its segment
Syntax is like this
Examples are
  val1 DB 255 ; largest unsigned value
  val2 DB +127 ; largest signed value
[name] DB initializer

## Slide 44: Defining BYTE and SBYTE Data
value1 BYTE 'A' ; character constant
value2 BYTE 0 ; smallest unsigned byte
value3 BYTE 255 ; largest unsigned byte
value4 SBYTE -128 ; smallest signed byte
value5 SBYTE +127 ; largest signed byte
value6 BYTE ? ; uninitialized byte
Each of the following defines a single byte of storage:
MASM does not prevent you from initializing a BYTE with a negative value, but it's considered poor style.
If you declare a SBYTE variable, the Microsoft debugger will automatically display its value in decimal with a leading sign.

## Slide 45: Multiple Initializers
If multiple initializers are used in the same data definition statement
  … its label refers only to the offset of first initializer
Also called Array
Example is
  vals1 DB 10, -20, 30
  vals2 DW 0Ah, 10, 00111100b
[name] Directive initializer ,initializer

## Slide 46: Defining Byte Arrays
list1 BYTE 10,20,30,40
list2 BYTE 10,20,30,40
BYTE 50,60,70,80
BYTE 81,82,83,84
list3 BYTE ?,32,41h,00100010b
list4 BYTE 0Ah,20h,‘A’,22h
Examples that use multiple initializers:

## Slide 47: Defining Strings (1 of 3)
A string is implemented as an array of characters
  For convenience, it is usually enclosed in quotation marks
  It often will be null-terminated
Examples:
str1 BYTE "Enter your name",0
str2 BYTE 'Error: halting program',0
str3 BYTE 'A','E','I','O','U'
greeting BYTE "Welcome to the Encryption Demo program "
BYTE "created by Kip Irvine.",0

## Slide 48: Defining Strings (2 of 3)
To continue a single string across multiple lines, end each line with a comma:
menu BYTE "Checking Account",0dh,0ah,0dh,0ah,
"1. Create a new account",0dh,0ah,
"2. Open an existing account",0dh,0ah,
"3. Credit the account",0dh,0ah,
"4. Debit the account",0dh,0ah,
"5. Exit",0ah,0ah,
"Choice> ",0

## Slide 49: Defining Strings (3 of 3)
End-of-line character sequence:
  0Dh = carriage return
  0Ah = line feed
str1 BYTE "Enter your name: ",0Dh,0Ah
BYTE "Enter your address: ",0
newLine BYTE 0Dh,0Ah,0
Idea: Define all strings used by your program in the same area of the data segment.

## Slide 50: Using the DUP Operator
Use DUP to allocate (create space for) an array or string. Syntax: counter DUP ( argument )
Counter and argument must be constants or constant expressions
var1 BYTE 20 DUP(0) ; 20 bytes, all equal to zero
var2 BYTE 20 DUP(?) ; 20 bytes, uninitialized
var3 BYTE 4 DUP("STACK") ; 20 bytes: "STACKSTACKSTACKSTACK"
var4 BYTE 10,3 DUP(0),20 ; 5 bytes

## Slide 51: DW Directive
Defines a 16-bit signed or unsigned integer
The initializer must fit into 16-bits either signed or unsigned
name shows the offset from the beginning of its segment
Syntax is like this
Examples are
  val1 DW 65535 ;largest unsigned value
  val2 DW -32768 ;smallest signed value
[name] DW initializer

## Slide 52: Defining WORD and SWORD Data
Define storage for 16-bit integers
  or double characters
  single value or multiple values
word1 WORD 65535 ; largest unsigned value
word2 SWORD –32768 ; smallest signed value
word3 WORD ? ; uninitialized, unsigned
word4 WORD "AB" ; double characters
myList WORD 1,2,3,4,5 ; array of words
array WORD 5 DUP(?) ; uninitialized array

## Slide 53: DD Directive
Defines a 32-bit signed or unsigned integer
The initializer must fit into 32-bits either signed or unsigned
name shows the offset from the beginning of its segment
Syntax is like this
Examples are
  val1 DD FFFFFFFFh ;largest unsigned value
  val2 DD 80000000h ;smallest signed value
[name] DD initializer

## Slide 54: Defining DWORD and SDWORD Data
val1 DWORD 12345678h ; unsigned
val2 SDWORD –2147483648 ; signed
val3 DWORD 20 DUP(?) ; unsigned array
val4 SDWORD –3,–2,–1,0,1 ; signed array
Storage definitions for signed and unsigned 32-bit integers:

## Slide 55: DQ Directive
Defines a 64-bit signed or unsigned integer
The initializer must fit into 64-bits either signed or unsigned
name shows the offset from the beginning of its segment
Syntax is like this
Examples are
  val1 DQ 10001010h
  val2 DQ 10001010b
[name] DQ initializer

## Slide 56: Defining QWORD, TBYTE, Real Data
quad1 QWORD 1234567812345678h
val1 TBYTE 1000000000123456789Ah
rVal1 REAL4 -2.1
rVal2 REAL8 3.2E-260
rVal3 REAL10 4.6E+4096
ShortArray REAL4 20 DUP(0.0)
Storage definitions for quadwords, tenbyte values, and real numbers:

## Slide 57: Little Endian Order
x86 processors store and retrieve data from memory using Little Endian Order
Least significant byte is stored at the first memory address allocated for data
Remaining bytes are stored in the next consecutive memory locations
Example, consider 2-bytes value 1234h
  If placed in memory at offset 0000, 34h would be stored in first byte
  12h would be stored in the second byte

## Slide 58: Little Endian Order
All data types larger than a byte store their individual bytes in reverse order. The least significant byte occurs at the first (lowest) memory address.
Example:
val1 DWORD 12345678h

## Slide 59: Big Endian Order
Some other processors store and retrieve data from memory using Big Endian Order
Most significant byte is stored at the first memory address allocated for data
Remaining bytes are stored in the next consecutive memory locations
Example, consider 2-bytes value 1234h
  If placed in memory at offset 0000, 12h would be stored in first byte
  34h would be stored in the second byte

## Slide 60: Adding Variables to AddSub
TITLE Add and Subtract, Version 2 (AddSub2.asm)
; This program adds and subtracts 32-bit unsigned
; integers and stores the sum in a variable.
INCLUDE Irvine32.inc
.data
val1 DWORD 10000h
val2 DWORD 40000h
val3 DWORD 20000h
finalVal DWORD ?
.code
main PROC
mov eax,val1 ; start with 10000h
  add eax,val2 ; add 40000h
  sub eax,val3 ; subtract 20000h
  mov finalVal,eax ; store the result (30000h)
  call DumpRegs ; display the registers
  exit
main ENDP
END main

## Slide 61: Declaring Unitialized Data
Use the .data? directive to declare an unintialized data segment:
  .data?
Within the segment, declare variables with "?" initializers:
  smallArray DWORD 10 DUP(?)
Advantage: the program's EXE file size is reduced.

## Slide 62: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 63: Symbolic Constants
Equal-Sign Directive
Calculating the Sizes of Arrays and Strings
EQU Directive
TEXTEQU Directive

## Slide 64: Equal-Sign Directive
name = expression
  expression is a 32-bit integer (expression or constant)
  may be redefined
  name is called a symbolic constant
good programming style to use symbols
COUNT = 500
.
.
mov ax,COUNT

## Slide 65: Calculating the Size of a Byte Array
current location counter: $
  subtract address of list
  difference is the number of bytes
list BYTE 10,20,30,40
ListSize = ($ - list)

## Slide 66: Calculating the Size of a Word Array
Divide total number of bytes by 2 (the size of a word)
list WORD 1000h,2000h,3000h,4000h
ListSize = ($ - list) / 2

## Slide 67: Calculating the Size of a Doubleword Array
Divide total number of bytes by 4 (the size of a doubleword)
list DWORD 1,2,3,4
ListSize = ($ - list) / 4

## Slide 68: EQU Directive
Define a symbol as either an integer or text expression.
Cannot be redefined
PI EQU <3.1416>
pressKey EQU <"Press any key to continue...",0>
.data
prompt BYTE pressKey

## Slide 69: TEXTEQU Directive
Define a symbol as either an integer or text expression.
Called a text macro
Can be redefined
continueMsg TEXTEQU <"Do you wish to continue (Y/N)?">
rowSize = 5
.data
prompt1 BYTE continueMsg
count TEXTEQU %(rowSize * 2) ; evaluates the expression
setupAL TEXTEQU <mov al,count>
.code
setupAL ; generates: "mov al,10"

## Slide 70: What's Next
Basic Elements of Assembly Language
Example: Adding and Subtracting Integers
Assembling, Linking, and Running Programs
Defining Data
Symbolic Constants
Real-Address Mode Programming

## Slide 71: Real-Address Mode Programming (1 of 2)
Generate 16-bit MS-DOS Programs
Advantages
  enables calling of MS-DOS and BIOS functions
  no memory access restrictions
Disadvantages
  must be aware of both segments and offsets
  cannot call Win32 functions (Windows 95 onward)
  limited to 640K program memory

## Slide 72: Real-Address Mode Programming (2 of 2)
Requirements
  INCLUDE Irvine16.inc
  Initialize DS to the data segment:
      mov ax,@data
      mov ds,ax

## Slide 73: Add and Subtract, 16-Bit Version
TITLE Add and Subtract, Version 2 (AddSub2r.asm)
INCLUDE Irvine16.inc
.data
val1 DWORD 10000h
val2 DWORD 40000h
val3 DWORD 20000h
finalVal DWORD ?
.code
main PROC
  mov ax,@data ; initialize DS
  mov ds,ax
  mov eax,val1 ; get first value
  add eax,val2 ; add second value
  sub eax,val3 ; subtract third value
  mov finalVal,eax ; store the result
  call DumpRegs ; display registers
  exit
main ENDP
END main

## Slide 74: Summary
Integer expression, character constant
directive – interpreted by the assembler
instruction – executes at runtime
code, data, and stack segments
source, listing, object, map, executable files
Data definition directives:
  BYTE, SBYTE, WORD, SWORD, DWORD, SDWORD, QWORD, TBYTE, REAL4, REAL8, and REAL10
  DUP operator, location counter ($)
Symbolic constant
  EQU and TEXTEQU

## Slide 75: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only