## Slide 1: Computer Organization & Assembly Language - EE2003

## Slide 2: Lecture 07
Week 04

## Slide 3: Data Transfer Instructions
Operand Types
Instruction Operand Notation
Direct Memory Operands
MOV Instruction
Zero & Sign Extension
XCHG Instruction
Direct-Offset Instructions

## Slide 4: Operand Types
Immediate – a constant integer (8, 16, or 32 bits)
  value is encoded within the instruction
Register – the name of a register
  register name is converted to a number and encoded within the instruction
Memory – reference to a location in memory
  memory address is encoded within the instruction, or a register holds the address of a memory location

## Slide 5: Instruction Operand Notation

## Slide 6: Direct Memory Operands
A direct memory operand is a named reference to storage in memory
The named reference (label) is automatically dereferenced by the assembler
.data
var1 BYTE 10h
.code
mov al,var1 ; AL = 10h
mov al,[var1] ; AL = 10h
alternate format

## Slide 7: MOV Instruction
.data
count BYTE 100
wVal WORD 2
.code
mov bl,count
mov ax,wVal
mov count,al
mov al,wVal ; error
mov ax,count ; error
mov eax,count ; error
Move from source to destination. Syntax:
    { MOV destination,source }
No more than one memory operand permitted
CS, EIP, and IP cannot be the destination
No immediate to segment moves

## Slide 8: MOV Instruction (2/2)
Some rules to follow when using MOV
  Both operands must have same size
  Both operands cannot be memory operands
  CS, EIP, IP cannot be destination operands
  An immediate value cannot be moved to a segment register
Some useful variants of MOV
MOV reg, reg
MOV reg, mem
MOV reg, imm
MOV mem, reg
MOV mem, imm

## Slide 9: Zero/Sign Extension of Integers (1/4)
MOV cannot copy data directly from a smaller operand to a larger one
Suppose we want to move a byte variable var into a 16-bit register ax
.data
var DB 10h
.code
MOV ax, 0
MOV al, var

## Slide 10: Zero/Sign Extension of Integers (2/4)
What happens if same approach is followed to copy a negative number?
What is the value in ax after this code is assembled?
.data
svar DB -8
.code
MOV ax, 0
MOV al, svar
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
248
What happened to -8?

## Slide 11: Zero/Sign Extension of Integers (3/4)
How about doing like this?
.data
svar DB -8
.code
MOV ax, 0FFFFFFFFh
MOV al, svar
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0
-8

## Slide 12: Zero/Sign Extension of Integers (4/4)
These examples show different approaches for signed and unsigned number
  In case of unsigned numbers, a zero is extended to all higher order bits of the destination operand
  In case of signed numbers, the sign-bit is extended to all higher order bits of the destination operand

## Slide 13: Your turn . . .
.data
bVal BYTE 100
bVal2 BYTE ?
wVal WORD 2
dVal DWORD 5
.code
mov ds,45
mov esi,wVal
mov eip,dVal
mov 25,bVal
mov bVal2,bVal
Explain why each of the following MOV statements are invalid:
immediate move to DS not permitted
size mismatch
EIP cannot be the destination
immediate value cannot be destination
memory-to-memory move not permitted

## Slide 14: Zero Extension
mov bl,10001111b
movzx ax,bl ; zero-extension
When you copy a smaller value into a larger destination, the MOVZX instruction fills (extends) the upper half of the destination with zeros.
The destination must be a register.

## Slide 15: MOVZX Instruction (1/2)
MOVZX (MOVe with Zero-eXtend) copies the source operand into destination operand and extends zeroes in the remaining higher order bits of destination operand
It has three variants
  MOVZX reg32, reg/mem8
  MOVZX reg32, reg/mem16
  MOVZX reg16, reg/mem8

## Slide 16: MOVZX Instruction (2/2)
.data
val DB 11000011b
.code
MOVZX ax, val
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0

## Slide 17: Sign Extension
mov bl,10001111b
movsx ax,bl ; sign extension
The MOVSX instruction fills the upper half of the destination with a copy of the source operand's sign bit.
The destination must be a register.

## Slide 18: MOVSX Instruction (1/2)
MOVSX (MOVe with Sign-eXtend) copies the source operand into destination operand and extends the sign-bit in remaining higher order bits in destination operand
It has three formats
  MOVSX reg32, reg/mem8
  MOVSX reg32, reg/mem16
  MOVSX reg16, reg/mem8

## Slide 19: MOVSX Instruction (2/2)
.data
val DB 11000011b
.code
MOVSX ax, val
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
.data
val DB 01000011b
.code
MOVSX ax, val

## Slide 20: LAHF and SAHD Instructions
LAHF (Load AH from status Flags) instruction copies lower byte of EFLAGS register into AH
Sign, Zero, Auxiliary Carry, Parity and Carry flags are copied
SAHF (Store AH into status Flags) instruction copies AH into lower byte of EFLAGS register

## Slide 21: XCHG Instruction
.data
var1 WORD 1000h
var2 WORD 2000h
.code
xchg ax,bx ; exchange 16-bit regs
xchg ah,al ; exchange 8-bit regs
xchg var1,bx ; exchange mem, reg
xchg eax,ebx ; exchange 32-bit regs
xchg var1,var2 ; error: two memory operands
XCHG exchanges the values of two operands. At least one operand must be a register. No immediate operands are permitted.

## Slide 22: XCHG Instruction
XCHG instruction exchanges the contents of two operands
This instruction has three different variants
  XCHG reg, reg
  XCHG reg, mem
  XCHG mem, reg
To exchange two memory operands, a register is used as temporary container
XCHG al, ah

## Slide 23: Direct-Offset Operands
Adding a displacement or offset to the name of a variable
This technique makes it possible to access memory locations which do not have explicit labels
For example, to access individual elements of an array

## Slide 24: Direct-Offset Operands
.data
arrayB BYTE 10h,20h,30h,40h
.code
mov al,arrayB+1 ; AL = 20h
mov al,[arrayB+1] ; alternative notation
A constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.
Q: Why doesn't arrayB+1 produce 11h?

## Slide 25: Direct-Offset Operands (cont)
.data
arrayW WORD 1000h,2000h,3000h
arrayD DWORD 1,2,3,4
.code
mov ax,[arrayW+2] ; AX = 2000h
mov ax,[arrayW+4] ; AX = 3000h
mov eax,[arrayD+4] ; EAX = 00000002h
A constant offset is added to a data label to produce an effective address (EA). The address is dereferenced to get the value inside its memory location.
; Will the following statements assemble?
mov ax,[arrayW-2] ; ??
mov eax,[arrayD+16] ; ??
What will happen when they run?

## Slide 26: Your turn. . .
Write a program that rearranges the values of three doubleword values in the following array as: 3, 1, 2.
  .data
  arrayD DWORD 1,2,3
Step 2: Exchange EAX with the third array value and copy the value in EAX to the first array position.
Step1: copy the first value into EAX and exchange it with the value in the second position.
mov eax,arrayD
xchg eax,[arrayD+4]
xchg eax,[arrayD+8]
mov arrayD,eax

## Slide 27: Evaluate this . . .
We want to write a program that adds the following three bytes:
.data
myBytes BYTE 80h,66h,0A5h
What is your evaluation of the following code?
mov al,myBytes
add al,[myBytes+1]
add al,[myBytes+2]
What is your evaluation of the following code?
mov ax,myBytes
add ax,[myBytes+1]
add ax,[myBytes+2]
Any other possibilities?

## Slide 28: Evaluate this . . . (cont)
.data
myBytes BYTE 80h,66h,0A5h
How about the following code. Is anything missing?
movzx ax,myBytes
mov bl,[myBytes+1]
add ax,bx
mov bl,[myBytes+2]
add ax,bx ; AX = sum
Yes: Move zero to BX before the MOVZX instruction.

## Slide 29: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only

## Slide 30: Lecture 08
Week 04

## Slide 31: What's Next
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions

## Slide 32: Addition and Subtraction
INC and DEC Instructions
ADD and SUB Instructions
NEG Instruction
Implementing Arithmetic Expressions
Flags Affected by Arithmetic
  Zero
  Sign
  Carry
  Overflow

## Slide 33: INC and DEC Instructions
Add 1, subtract 1 from destination operand
  operand may be register or memory
INC destination
    Logic: destination  destination + 1
DEC destination
    Logic: destination  destination – 1

## Slide 34: INC and DEC Instructions
INC instruction increments 1 in a single operand
DEC instruction decrements 1 from a single operand
Syntax is
  INC reg/mem
  DEC reg/mem
Flags affected
  OF, SF, ZF, AF, PF

## Slide 35: INC and DEC Examples
.data
myWord WORD 1000h
myDword DWORD 10000000h
.code
inc myWord ; 1001h
dec myWord ; 1000h
inc myDword ; 10000001h
mov ax,00FFh
inc ax ; AX = 0100h
mov ax,00FFh
inc al ; AX = 0000h

## Slide 36: Your turn...
Show the value of the destination operand after each of the following instructions executes:
.data
myByte BYTE 0FFh, 0
.code
mov al,myByte ; AL =
mov ah,[myByte+1] ; AH =
dec ah ; AH =
inc al ; AL =
dec ax ; AX =
FFh
00h
FFh
00h
FEFF

## Slide 37: ADD and SUB Instructions
ADD destination, source
  Logic: destination  destination + source
SUB destination, source
  Logic: destination  destination – source
Same operand rules as for the MOV instruction

## Slide 38: ADD Instruction
Adds a source operand into a destination operand
Both operands must have the same size
Sum is stored in the destination operand
Syntax is
Flags affected
  CF, ZF, SF, OF, AF, PF
ADD dest, src

## Slide 39: SUB Instruction
Subtracts a source operand from a destination operand
Both operands must have the same size
Result is stored in the destination operand
Syntax is
Flags affected
  CF, ZF, SF, OF, AF, PF
SUB dest, src

## Slide 40: ADD and SUB Examples
.data
var1 DWORD 10000h
var2 DWORD 20000h
.code ; ---EAX---
mov eax,var1 ; 00010000h
add eax,var2 ; 00030000h
add ax,0FFFFh ; 0003FFFFh
add eax,1 ; 00040000h
sub ax,1 ; 0004FFFFh

## Slide 41: NEG (negate) Instruction
.data
valB BYTE -1
valW WORD +32767
.code
mov al,valB ; AL = -1
neg al ; AL = +1
neg valW ; valW = -32767
Reverses the sign of an operand. Operand can be a register or memory operand.
Suppose AX contains –32,768 and we apply NEG to it. Will the result be valid?

## Slide 42: NEG Instruction
Reverses the sign of a number by taking its 2’s complement
Syntax is
  NEG reg
  NEG mem
Flags affected
  CF, ZF, SF, OF, AF, PF

## Slide 43: NEG Instruction and the Flags
.data
valB BYTE 1,0
valC SBYTE -128
.code
neg valB ; CF = 1, OF = 0
neg [valB + 1] ; CF = 0, OF = 0
neg valC ; CF = 1, OF = 1
The processor implements NEG using the following internal operation:
SUB 0,operand
Any nonzero operand causes the Carry flag to be set.

## Slide 44: Implementing Arithmetic Expressions
Rval DWORD ?
Xval DWORD 26
Yval DWORD 30
Zval DWORD 40
.code
mov eax,Xval
neg eax ; EAX = -26
mov ebx,Yval
sub ebx,Zval ; EBX = -10
add eax,ebx
mov Rval,eax ; -36
HLL compilers translate mathematical expressions into assembly language. You can do it also. For example:
Rval = -Xval + (Yval – Zval)

## Slide 45: Your turn...
mov ebx,Yval
neg ebx
add ebx,Zval
mov eax,Xval
sub eax,ebx
mov Rval,eax
Translate the following expression into assembly language. Do not permit Xval, Yval, or Zval to be modified:
Rval = Xval - (-Yval + Zval)
Assume that all values are signed doublewords.

## Slide 46: Flags Affected by Arithmetic
The ALU has a number of status flags that reflect the outcome of arithmetic (and bitwise) operations
  based on the contents of the destination operand
Essential flags:
  Zero flag – set when destination equals zero
  Sign flag – set when destination is negative
  Carry flag – set when unsigned value is out of range
  Overflow flag – set when signed value is out of range
The MOV instruction never affects the flags.

## Slide 47: Concept Map
status flags
ALU
conditional jumps
branching logic
arithmetic & bitwise operations
part of
used by
provide
attached to
affect
CPU
You can use diagrams such as these to express the relationships between assembly language concepts.
executes
executes

## Slide 48: Zero Flag (ZF)
ZF is set when the result of an operation produces zero in the destination operand
Remember that
  A flag is set when it equals 1
  A flag is clear when it equals 0
MOV al, 1
SUB al, 1
MOV bl, 0FFh
INC bl
INC bl
;no flag affected
;al=0  ZF=1
;no flag affected
;bl=0  ZF=1
;bl=1  ZF=0

## Slide 49: Zero Flag (ZF)
mov cx,1
sub cx,1 ; CX = 0, ZF = 1
mov ax,0FFFFh
inc ax ; AX = 0, ZF = 1
inc ax ; AX = 1, ZF = 0
The Zero flag is set when the result of an operation produces zero in the destination operand.
Remember...
A flag is set when it equals 1.
A flag is clear when it equals 0.

## Slide 50: Sign Flag (SF)
SF is set when destination operand is –ve
SF is clear when destination is +ve
MOV al, 0
SUB al, 1
ADD al, 2
;no flag affected
;al=-1  SF=1
;al=1  SF=0

## Slide 51: Sign Flag (SF)
mov cx,0
sub cx,1 ; CX = -1, SF = 1
add cx,2 ; CX = 1, SF = 0
The Sign flag is set when the destination operand is negative. The flag is clear when the destination is positive.
The sign flag is a copy of the destination's highest bit:
mov al,0
sub al,1 ; AL = 11111111b, SF = 1
add al,2 ; AL = 00000001b, SF = 0

## Slide 52: Signed and Unsigned Integers A Hardware Viewpoint
All CPU instructions operate exactly the same on signed and unsigned integers
The CPU cannot distinguish between signed and unsigned integers
YOU, the programmer, are solely responsible for using the correct data type with each instruction

## Slide 53: Overflow and Carry Flags A Hardware Viewpoint
How the ADD instruction affects OF and CF:
  CF = (carry out of the MSB)
  OF = CF XOR MSB
How the SUB instruction affects OF and CF:
  CF = INVERT (carry out of the MSB)
  negate the source and add it to the destination
  OF = CF XOR MSB
MSB = Most Significant Bit (high-order bit)
XOR = eXclusive-OR operation
NEG = Negate (same as SUB 0,operand )

## Slide 54: Carry Flag (CF)
The Carry flag is set when the result of an operation generates an unsigned value that is out of range (too big or too small for the destination operand).
mov al,0FFh
add al,1 ; CF = 1, AL = 00
; Try to go below zero:
mov al,0
sub al,1 ; CF = 1, AL = FF

## Slide 55: Your turn . . .
mov ax,00FFh
add ax,1 ; AX= SF= ZF= CF=
sub ax,1 ; AX= SF= ZF= CF=
add al,1 ; AL= SF= ZF= CF=
mov bh,6Ch
add bh,95h ; BH= SF= ZF= CF=
mov al,2
sub al,3 ; AL= SF= ZF= CF=
For each of the following marked entries, show the values of the destination operand and the Sign, Zero, and Carry flags:
0100h 0 0 0
00FFh 0 0 0
00h 0 1 1
01h 0 0 1
FFh 1 0 1

## Slide 56: Overflow Flag (OF)
The Overflow flag is set when the signed result of an operation is invalid or out of range.
; Example 1
mov al,+127
add al,1 ; OF = 1, AL = ??
; Example 2
mov al,7Fh ; OF = 1, AL = 80h
add al,1
The two examples are identical at the binary level because 7Fh equals +127. To determine the value of the destination operand, it is often easier to calculate in hexadecimal.

## Slide 57: A Rule of Thumb
When adding two integers, remember that the Overflow flag is only set when . . .
  Two positive operands are added and their sum is negative
  Two negative operands are added and their sum is positive
What will be the values of the Overflow flag?
mov al,80h
add al,92h ; OF =
mov al,-2
add al,+127 ; OF =
1
0

## Slide 58: Your turn . . .
mov al,-128
neg al ; CF = OF =
mov ax,8000h
add ax,2 ; CF = OF =
mov ax,0
sub ax,2 ; CF = OF =
mov al,-5
sub al,+125 ; OF =
What will be the values of the given flags after each operation?
1 1
0 0
1 0
1

## Slide 59: What's Next
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions

## Slide 60: Data-Related Operators and Directives
OFFSET Operator
PTR Operator
TYPE Operator
LENGTHOF Operator
SIZEOF Operator

## Slide 61: OFFSET Operator
OFFSET returns the distance in bytes, of a label from the beginning of its enclosing segment
  Protected mode: 32 bits
  Real mode: 16 bits
The Protected-mode programs we write use only a single segment (flat memory model).

## Slide 62: OFFSET Examples
.data
bVal BYTE ?
wVal WORD ?
dVal DWORD ?
dVal2 DWORD ?
.code
mov esi,OFFSET bVal ; ESI = 00404000
mov esi,OFFSET wVal ; ESI = 00404001
mov esi,OFFSET dVal ; ESI = 00404003
mov esi,OFFSET dVal2 ; ESI = 00404007
Let's assume that the data segment begins at 00404000h:

## Slide 63: Relating to C/C++
// C++ version:
char array[1000];
char * p = array;
The value returned by OFFSET is a pointer. Compare the following code written for both C++ and assembly language:
; Assembly language:
.data
array BYTE 1000 DUP(?)
.code
mov esi,OFFSET array

## Slide 64: PTR Operator
.data
myDouble DWORD 12345678h
.code
mov ax,myDouble ; error – why?
mov ax,WORD PTR myDouble ; loads 5678h
mov WORD PTR myDouble,4321h ; saves 4321h
Overrides the default type of a label (variable). Provides the flexibility to access part of a variable.
Little endian order is used when storing data in memory (see Section 3.4.9).

## Slide 65: Little Endian Order
Little endian order refers to the way Intel stores integers in memory.
Multi-byte integers are stored in reverse order, with the least significant byte stored at the lowest address
For example, the doubleword 12345678h would be stored as:
When integers are loaded from memory into registers, the bytes are automatically re-reversed into their correct positions.

## Slide 66: PTR Operator Examples
.data
myDouble DWORD 12345678h
mov al,BYTE PTR myDouble ; AL = 78h
mov al,BYTE PTR [myDouble+1] ; AL = 56h
mov al,BYTE PTR [myDouble+2] ; AL = 34h
mov ax,WORD PTR myDouble ; AX = 5678h
mov ax,WORD PTR [myDouble+2] ; AX = 1234h

## Slide 67: PTR Operator (cont)
.data
myBytes BYTE 12h,34h,56h,78h
.code
mov ax,WORD PTR [myBytes] ; AX = 3412h
mov ax,WORD PTR [myBytes+2] ; AX = 7856h
mov eax,DWORD PTR myBytes ; EAX = 78563412h
PTR can also be used to combine elements of a smaller data type and move them into a larger operand. The CPU will automatically reverse the bytes.

## Slide 68: Your turn . . .
.data
varB BYTE 65h,31h,02h,05h
varW WORD 6543h,1202h
varD DWORD 12345678h
.code
mov ax,WORD PTR [varB+2] ; a.
mov bl,BYTE PTR varD ; b.
mov bl,BYTE PTR [varW+2] ; c.
mov ax,WORD PTR [varD+2] ; d.
mov eax,DWORD PTR varW ; e.
Write down the value of each destination operand:
0502h
78h
02h
1234h
12026543h

## Slide 69: TYPE Operator
The TYPE operator returns the size, in bytes, of a single element of a data declaration.
.data
var1 BYTE ?
var2 WORD ?
var3 DWORD ?
var4 QWORD ?
.code
mov eax,TYPE var1 ; 1
mov eax,TYPE var2 ; 2
mov eax,TYPE var3 ; 4
mov eax,TYPE var4 ; 8

## Slide 70: LENGTHOF Operator
.data LENGTHOF
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 32
array2 WORD 5 DUP(3 DUP(?)) ; 15
array3 DWORD 1,2,3,4 ; 4
digitStr BYTE "12345678",0 ; 9
.code
mov ecx,LENGTHOF array1 ; 32
The LENGTHOF operator counts the number of elements in a single data declaration.

## Slide 71: SIZEOF Operator
.data SIZEOF
byte1 BYTE 10,20,30 ; 3
array1 WORD 30 DUP(?),0,0 ; 64
array2 WORD 5 DUP(3 DUP(?)) ; 30
array3 DWORD 1,2,3,4 ; 16
digitStr BYTE "12345678",0 ; 9
.code
mov ecx,SIZEOF array1 ; 64
The SIZEOF operator returns a value that is equivalent to multiplying LENGTHOF by TYPE.

## Slide 72: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only

## Slide 73: Lecture 09
Week 05

## Slide 74: What's Next
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions

## Slide 75: Indirect Addressing
Indirect Operands
Array Sum Example
Indexed Operands

## Slide 76: Indirect Operands (1/3)
In Protected Mode
  A 32-bit general purpose register can be used as an indirect operand surrounded by square brackets
  The register contains the address of variable
In Real-Address Mode
  A 16-bit register holds the offset of variable
  Any of SI, DI, BX or BP can be used
Indirect Operands are useful to step through arrays

## Slide 77: Indirect Operands (2/3)
.data
val DB 10h, 20h, 30h
.code
MOV esi, OFFSET val
MOV al, [esi]
INC esi
MOV bl, [esi]
Protected Mode

## Slide 78: Indirect Operands (3/3)
Real-Address Mode
.data
val DB 10h, 20h, 30h
.code
MOV si, OFFSET val
MOV al, [si]
INC si
MOV bl, [si]

## Slide 79: Pointer
A pointer can be declared in the following way
.data
val DW 10h
vptr DW val
.code
MOV si, vptr
MOV al, [si]

## Slide 80: Indirect Operands (1 of 2)
.data
val1 BYTE 10h,20h,30h
.code
mov esi,OFFSET val1
mov al,[esi] ; dereference ESI (AL = 10h)
inc esi
mov al,[esi] ; AL = 20h
inc esi
mov al,[esi] ; AL = 30h
An indirect operand holds the address of a variable, usually an array or string. It can be dereferenced (just like a pointer).

## Slide 81: Indirect Operands (2 of 2)
.data
myCount WORD 0
.code
mov esi,OFFSET myCount
inc [esi] ; error: ambiguous
inc WORD PTR [esi] ; ok
Use PTR to clarify the size attribute of a memory operand.
Should PTR be used here?
add [esi],20
yes, because [esi] could point to a byte, word, or doubleword

## Slide 82: Array Sum Example
.data
arrayW WORD 1000h,2000h,3000h
.code
  mov esi,OFFSET arrayW
  mov ax,[esi]
  add esi,2 ; or: add esi,TYPE arrayW
  add ax,[esi]
  add esi,2
  add ax,[esi] ; AX = sum of the array
Indirect operands are ideal for traversing an array. Note that the register in brackets must be incremented by a value that matches the array type.
ToDo: Modify this example for an array of doublewords.

## Slide 83: Indexed Operands
.data
arrayW WORD 1000h,2000h,3000h
.code
mov esi,0
mov ax,[arrayW + esi] ; AX = 1000h
mov ax,arrayW[esi] ; alternate format
add esi,2
add ax,[arrayW + esi]
etc.
An indexed operand adds a constant to a register to generate an effective address. There are two notational forms:
[label + reg] label[reg]
ToDo: Modify this example for an array of doublewords.

## Slide 84: Index Scaling
.data
arrayB BYTE 0,1,2,3,4,5
arrayW WORD 0,1,2,3,4,5
arrayD DWORD 0,1,2,3,4,5
.code
mov esi,4
mov al,arrayB[esi*TYPE arrayB] ; 04
mov bx,arrayW[esi*TYPE arrayW] ; 0004
mov edx,arrayD[esi*TYPE arrayD] ; 00000004
You can scale an indirect or indexed operand to the offset of an array element. This is done by multiplying the index by the array's TYPE:

## Slide 85: What's Next
Data Transfer Instructions
Addition and Subtraction
Data-Related Operators and Directives
Indirect Addressing
JMP and LOOP Instructions

## Slide 86: JMP and LOOP Instructions
JMP Instruction
LOOP Instruction
LOOP Example
Summing an Integer Array
Copying a String

## Slide 87: JMP Instruction
top:
.
.
jmp top
JMP is an unconditional jump to a label that is usually within the same procedure.
Syntax: JMP target
Logic: EIP  target
Example:
A jump outside the current procedure must be to a special type of label called a global label (see Section 5.5.2.3 for details).

## Slide 88: LOOP Instruction
The LOOP instruction creates a counting loop
Syntax: LOOP target
Logic:
  ECX  ECX – 1
  if ECX != 0, jump to target
Implementation:
  The assembler calculates the distance, in bytes, between the offset of the following instruction and the offset of the target label. It is called the relative offset.
  The relative offset is added to EIP.

## Slide 89: LOOP Example
00000000 66 B8 0000 mov ax,0
00000004 B9 00000005 mov ecx,5
00000009 66 03 C1 L1: add ax,cx
0000000C E2 FB loop L1
0000000E
The following loop calculates the sum of the integers 5 + 4 + 3 +2 + 1:
When LOOP is assembled, the current location = 0000000E (offset of the next instruction). –5 (FBh) is added to the the current location, causing a jump to location 00000009:
00000009  0000000E + FB
Offset machine code source code

## Slide 90: Your turn . . .
If the relative offset is encoded in a single signed byte,
(a) what is the largest possible backward jump?
(b) what is the largest possible forward jump?
-128
+127

## Slide 91: Your turn . . .
What will be the final value of AX?
mov ax,6
mov ecx,4
L1:
inc ax
loop L1
How many times will the loop execute?
mov ecx,0
X2:
inc ax
loop X2
10
4,294,967,296

## Slide 92: Nested Loop
If you need to code a loop within a loop, you must save the outer loop counter's ECX value. In the following example, the outer loop executes 100 times, and the inner loop 20 times.
.data
count DWORD ?
.code
mov ecx,100 ; set outer loop count
L1:
mov count,ecx ; save outer loop count
mov ecx,20 ; set inner loop count
L2: .
  .
  loop L2 ; repeat the inner loop
mov ecx,count ; restore outer loop count
loop L1 ; repeat the outer loop

## Slide 93: Summing an Integer Array
.data
intarray WORD 100h,200h,300h,400h
.code
  mov edi,OFFSET intarray ; address of intarray
  mov ecx,LENGTHOF intarray ; loop counter
  mov ax,0 ; zero the accumulator
L1:
  add ax,[edi] ; add an integer
  add edi,TYPE intarray ; point to next integer
loop L1 ; repeat until ECX = 0
The following code calculates the sum of an array of 16-bit integers.

## Slide 94: Your turn . . .
What changes would you make to the program on the previous slide if you were summing a doubleword array?

## Slide 95: Copying a String
.data
source BYTE "This is the source string",0
target BYTE SIZEOF source DUP(0)
.code
mov esi,0 ; index register
mov ecx,SIZEOF source ; loop counter
L1:
mov al,source[esi] ; get char from source
mov target[esi],al ; store it in the target
inc esi ; move to next character
loop L1 ; repeat for entire string
good use of SIZEOF
The following code copies a string from source to target:

## Slide 96: Your turn . . .
Rewrite the program shown in the previous slide, using indirect addressing rather than indexed addressing.

## Slide 97: Summary
Data Transfer
  MOV – data transfer from source to destination
  MOVSX, MOVZX, XCHG
Operand types
  direct, direct-offset, indirect, indexed
Arithmetic
  INC, DEC, ADD, SUB, NEG
  Sign, Carry, Zero, Overflow flags
Operators
  OFFSET, PTR, TYPE, LENGTHOF, SIZEOF, TYPEDEF
JMP and LOOP – branching instructions

## Slide 98: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only

## Slide 99: Lecture 10
Week 05

## Slide 100
Quiz…

## Slide 102
Let's
Revise!

## Slide 103: THANKS!
Any questions?
You can find me at:
A.qadeer@nu.edu.pk
Office #213, Visiting Hours Only